ECSE-4790 Microprocessor Systems

8051 IDE Use & SDCC C Compiler

by Alexey Gutin (revised 8/2011)

References

SDCC Compiler User Guide; C8051F12x Development Kit User's Guide; C8051F120 Reference Manual; C8051F120.h; SDCC libdoc.txt; ASCII table. (These last 3 are attached at the end of this file.)

Introduction

In MPS we you will be developing code for the C8051F120 EVB (evaluation board). This board is from Silicon Laboratories (SiLabs). For that purpose, you will be using a x86 based PC (your laptop, a desktop, or coprocessor card in a Sun Ultra 10 workstation) to write and compile the controller programs. This type of development is called Cross Platform Development. After generating the machine code for the target environment and before you can run it you must download it to the C8051F120.

When doing cross platform development, extra knowledge of the target environment is needed. It is important to be able to answer the following questions:

- What is the target processor?

Silicon Laboratories C8051F120	(http://www.silabs.com)

- What memory resources does the execution environment have?

128 kBytes of FLASH ROM that extends from 00000 to 0x1FFFF and 8 kBytes of RAM. The compiler - and more specifically the linker - have been configured to make use of this memory address space.

- Are we dealing with only hardware or is there an interface program we have to go through?

All communication to the C8051F120 evaluation board is currently through the IDE (integrated development environment) from Silicon Laboratories running on the PC.

The SiLabs IDE is a convenient way to edit, compile, and download source code written for the microcontroller.  While SiLabs provides a nice interface for making source code changes and easily downloading them to the development boards, it lacks the actual compiler portion that converts C code into hex files, the common format used by the 8051.  To do this, a free and widely used open source tool called Small Device C Compiler (SDCC) is used.  SDCC compiles the C code written, and automatically optimizes and converts it to hex.  Due to its popularity, support for SDCC in the SiLabs IDE comes standard, making it easy and convenient to use.

Installing SDCC

To install SDCC, follow the simple instructions below:

- Open the following URL: http://sdcc.sourceforge.net/ . Click on the Download link under SDCC Home, and click on Sourceforge download page.  Download the latest under Download Now! (should be the latest package version for Windows).  A copy can also be obtained from the course website:

http://www.ecse.rpi.edu/courses/CStudio/SDCC%20Compiler/sdcc-2.9.0-setup.exe

- Open the executable that was just downloaded and allow the installation wizard to step you through the process of installing SDCC on your computer. It is recommended that you leave all of the configuration options and installation paths the same as suggested by the installation wizard, so that it will be easier to assist you should problems arise.

- To ensure SDCC was properly installed, click on:

Start Menu(All Programs

and ensure that SDCC shows up on your programs list. If it does, you have successfully installed SDCC.

Installing SiLabs IDE

To install the SiLabs IDE, follow the simple instructions below:

- Open the following URL:

http://www.silabs.com/products/mcu/Pages/8-bit-microcontroller-software.aspx Click on Silicon Labs IDE (under Download Now). A copy can also be obtained from the course website:

http://www.ecse.rpi.edu/courses/CStudio/Silabs/mcu_ide_4.10.exe .

- Open the executable that just downloaded and allow the installation wizard to step you through the installation process. Once again, it is recommended that you leave everything at the default settings. If this is a second install – check the “Maintain or update the instance of this application …”

- To check that SDCC was properly installed, click on:

Start Menu(All Programs

and ensure that Silicon Laboratories shows up on your programs list. If it does, you have successfully installed the SiLabs IDE.

Configuring SiLabs IDE with SDCC

To configure SDCC as the compiler in the SiLabs IDE, follow the instructions below:

- Click on:

Start(All Programs(Silicon Laboratories(Silicon Laboratories IDE

- Once open, click on:

Projects(Tool Chain Integration

- You will see a Preset Name dropdown box under Tool Definition Presets. Select SDCC 3.x from this menu. The values under Tool Definition should all change to the correct defaults.

- Next, you will notice that the Assembler tab is selected by default. Click on Browse to tell SiLabs where SDCC is installed. If you kept all the paths to the default as recommended, the path should be: 
	C:\Program Files\SDCC\bin\sdas8051.exe       (or asx8051.exe)

For Windows 7 it may be: C:\Program Files (x86)\SDCC\bin\sdas8051.exe

- After the assembler path is configured, you will need to configure the compiler path. To do this, click on the Compiler tab. Once again, click Browse and select the path to where SDCC is installed. If you kept all the paths to their defaults, the full path should be:
	C:\Program Files\SDCC\bin\sdcc.exe

For Windows 7 it may be: C:\Program Files (x86)\SDCC\bin\sdcc.exe

Check the Command line flags and replace “-l"C:SiLabs/MCU/inc"” with “--nogcse”, leaving all other existing flags as they were ( should be: -c --debug --use-stdout -V --nogcse).

- Finally, to configure the linker, select the Linker tab. Click Browse and select the path where SDCC is installed. The full path for a default installation should be:
	C:\Program Files\SDCC\bin\sdcc.exe

For Windows 7 it may be: C:\Program Files (x86)\SDCC\bin\sdcc.exe

The linker flags should be: --debug --use-stdout -V

- Once you have made these changes, click on Save As under Tool Definition Presets, enter MPS as the Preset Name and click OK. Now click OK in the Tool Chain Integration panel. It is very important that you do not change anything outside of what has been mentioned above, especially the command line flags passed to SDCC. Unfortunately, whenever a new project is created (see below), you must select MPS as the Preset Name and select No for Save Modified Presets. This seems to be a bug in the current IDE, otherwise it will not default to these correct MPS settings.

- You have successfully set up SiLabs IDE to use SDCC!

Creating a Project

NOTE: project files have the extension .wsp. Clicking on this file will start up the SiLabs IDE.

- Copy C source code into a text file with a .c extension (ex. Hello.c) and move it to a desired folder to be used for the new project (ex. C:\SiLabs\NEW_PROJ).

- To create a new project, click on:

Project(New Project…

Pick C8051F12x_13x in the “New” window for Select Device Family:, specify a Project Name: (ex. NEW_PROJ), then select the Location: (ex. C:\SiLabs\NEW_PROJ), set Project Type: to Blank Project, and click OK. This will create an empty project.

- Use Project(Add Files to Project… to add your C source file (ex. Hello.c) and header file (putget.h) to the project. After this, right-click on the source file name in the left side “File …” window and select Add xxx to build. Do the same with the header file.

- The file will now be part of the project, and can be compiled. Save the project by clicking on:

Project(Save Project

5.	The SDCC has some default compiler flags that may cause trouble in programs using interrupt routines. To turn off those features, make sure you made the changes to Tool Chain Integration outlined above in Configuring SiLabs IDE with SDCC. Unfortunately, you may need to specify MPS in Tool Definition Presets for every new project; the defaults can’t seem to be changed on some installations.

Compiling a Project

You will be using the SDCC cross compiler. The compiler generates executable files with the extension .exe from the C source files.

To create an executable program that runs on the C8051F120 processor from C code, there are three steps that must be taken. First the compiler takes the C source file (.c) and creates an object file (.hex). A linker takes the object file from the compiler and adds in the language library routines to create a link file. Finally a hex converter (or loader) takes the link file and generates a downloadable executable file that can be passed to the C8051F120 by the IDE. The IDE program downloads the .out file into the C8051F120 for execution.

Fortunately there are menu items that will perform all these operations. For a C source file in an opened IDE Project, the menu commands to generate the .exe download file are:

- To compile your project, first verify that all of your code is correct. If it’s not, don’t worry, the compiler will catch your mistakes.

- Click on:

Project(Assemble/Compile File	(<Ctrl><F7> or icon)

This will compile your project source code. The window at the bottom of the IDE will alert you of any errors or warnings it finds in your code. If there are errors, correct them first before moving on to the next step. If there are warnings, you may or may not want to correct them, depending on the nature of the warning.

- Next click on:

Project(Build/Make Project	(<F7> or icon)

This will link your compiled file. Any errors detected by the linker will be displayed.

Transferring the Executable Machine Code to the C8051F120

- After successfully building your project, you will want to download it to the development board. Before doing this, you will need to configure the adapter used to download the source code and establish the connection. First plug in the USB Debug Adapter. Then to establish a connection, click on:

Options(Connection Options

Once the window opens, select the USB Debug Adapter, make sure that JTAG is selected under Debug Interface (not C2), and click OK.

- To establish the connection to the 8051, make sure the USB Debug Adapter is plugged in, and then click on:

Debug(Connect

This will connect the IDE to the development board through the USB Debug Adapter.

- Click on:

Debug(Download Object File	(<Alt><D> or icon)

This will download the code to the development board.

Executing the Program on the C8051F120

Finally, to execute your code on the C8051F120, click on:

Debug(Go (or click the green button)

Note: to reset a program after stopping it, go to Debug(Reset or <Ctrl><R>.

ASCII Terminal Programs

We have two packages through which the C8051F120 board may communicate with the PC using the RS232 UART ports - HyperTerminal and ProComm Plus. To begin the process, start either HyperTerminal or ProComm Plus as a dumb terminal for the EVB.

Run the program ProComm Plus from Program Files(Procomm Plus(Data Terminal and HYPERTRM.EXE is started with Program Files(Accessories(HyperTerminal. HyperTerminal requires you to create a new connection configured for a direct connection to COM1 (no modem) with 115200 bits per second, 8 data bits, no (none) parity, 1 stop bit, and no (none) flow control (handshaking).

Connect the DB-9 serial cable from the PC card serial port, labeled COM1, to the serial port on the EVB.

IDE File Location Requirement

In order to work correctly, your project files should be in the C:\SiLabs directory. The header files (.h) are in C:\Program Files\SDCC\include and the compiler (sdcc.exe), linker and make file (makebin.exe) are located in C:\Program Files\SDCC\bin.

PROGRAMMING HINT

Normal termination of a program occurs when the last line in main() is executed. This is done at the end of a program by calling the function:

return;

at which point the program will stop but the Halt button in the IDE must still be selected.

SDCC Quirks & Problems

1.	Make sure you are on the correct SFR page for the F120 processor when accessing SFRs. Very unexpected results may occur without any errors or warning from writing to other SFRs with the same numerical ID that reside on different SFR pages. This should apply to sbits too. The sbit is only available on the SFR’s page.

2.	#define values shouldn’t end with a “;” Doing so will create problems in some C statements. For example:

int test;

#define VALUE = 1234;	//This should be: #define VALUE = 1234

…

test = 4321;

if(test < VALUE)...		//This will not work, it is equivalent to “if(test < 1234;)…”

//Also, #define variables may not be used to set the values of s-bits.

3.	To create an sbit or sfr with a specific name, SDCC uses the format:

sbit at 0xHH bit_name;	//0xHH is the hex value from the sbit table below in the

//SFR & SBIT DEFINITIONS table starting on page 9,

//bit_name is the label you choose for your variable

sfr at 0xHH sfr_name;	//NOTE: you still must be on the correct SFR page!

Again, sbit values are dependent on the SFR page; make sure you are on the correct page.

4.	To print floating point numbers, use:

printf_fast_f(“ f10.5”, 3.14159);	//Don’t use printf(), it will not work!

5.	Type conversion, especially implicit, may not work correctly. To extract numerical values of characters use atoi( ) & itoa( ) in stdlib.h.

6.	To define data in external RAM at a given address use:

xdata at 0x8EED int my_number;		//Will appear at address 0x8EED

The SDCC only allocates 128 bytes for program variable space. Creating too many variables will result in an error concerning limited memory. Moving some variables to external RAM can fix this error.

7.	Using too many variables, too large arrays, or too many large numerical types (long int, float, double) may result in a linker error “Could not get nn consecutive bytes in internal RAM for area DSEG”. To correct this the number and/or size of the variables must be reduced. Reuse variables in multiple calculations, reduce integers to short int or char if the maximum numerical value will fit in the smaller type and reduce the size of arrays if fewer elements will work. Also consider moving data into external RAM (as in 6. above).

8.	There is no implementation of the function scanf( ) in SDCC and there is no simple substitution. Any input must be done character by character using getchar( ) and extra processing by the program. Similarly, putchar( ) and getchar( ) are not directly available under SDCC. As mentioned in the first lab exercise, include putget.h in all programs to retain these functions.

9.	A program that resets and restarts randomly or seems to lose the value of variables may be a result of the watchdog interrupt not being disabled. Make sure the 2 statements needed to kill the watchdog are included in your system initialization.

10.	Unreachable code warnings may show up as a result of temporarily disabling sections of code in the process of debugging programs. These may be ignored.

11.	Sbit variables can’t be initialized when they are defined. This will generate a lot of random assembler errors. Set them equal to 0 or 1 on a separate line inside main(). Likewise arrays that are attempted to be initialized by a statement such as “char Data[2] = 0;” will generate unrelated error messages complaining about structures that don’t exist and the flagged lines may move about randomly. Use “char Data[2] = {0, 0};”. On occasion initializing declared variables in xdata has been troublesome. Be aware that these might not be initialing properly.

12.	All local variables must be declared at the beginning of the routine (main or function). Implicit declaration at the time of use is not allowed. (But the latest version of SDCC may allow this.)

13.	File names cannot include the ‘#’ or ‘,’ characters and possibly other special characters. For some reason it tries to use the assembler on the C source code and generates many errors.

14.	As with most C compilers, the order of the included header files at the top of a program is important. Basic headers defining objects used in other headers MUST be included first. Most user created headers should be included last.

15.	With version 4.10 of the IDE and 2.9.0 of SDCC there are a number of new issues. If multiple .c & .h files are used in a project and added to the build, it is possible to confuse the compiler and linker so that it doesn’t know which file contains main( ), and it may actually try to run some other function as main, yielding very unexpected results. When adding files to the build, make sure the icon changes to “the-file-to-be-built” icon for the file containing main( ).

C8051F120.h – SFR & SBIT DEFINITIONS

/*---------------------------------------------------------------------------

Register Declarations for the Cygnal/SiLabs C8051F12x-F13x Processor Range

Copyright (C) 2003 - Maarten Brock, sourceforge.brock@dse.nl

This library is free software; you can redistribute it and/or

modify it under the terms of the GNU Lesser General Public

License as published by the Free Software Foundation; either

version 2.1 of the License, or (at your option) any later version.

This library is distributed in the hope that it will be useful,

but WITHOUT ANY WARRANTY; without even the implied warranty of

MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE.  See the GNU

Lesser General Public License for more details.

You should have received a copy of the GNU Lesser General Public

License along with this library; if not, write to the Free Software

Foundation, Inc., 59 Temple Place, Suite 330, Boston, MA  02111-1307 USA

---------------------------------------------------------------------------*/

#ifndef C8051F120_H

#define C8051F120_H

/*  BYTE Registers  */

/*  All Pages */

__sfr __at (0x80) P0               ;  /* PORT 0                                        */

__sfr __at (0x81) SP               ;  /* STACK POINTER                                 */

__sfr __at (0x82) DPL              ;  /* DATA POINTER - LOW BYTE                       */

__sfr __at (0x83) DPH              ;  /* DATA POINTER - HIGH BYTE                      */

__sfr __at (0x84) SFRPAGE          ;  /* SFR PAGE SELECT                               */

__sfr __at (0x85) SFRNEXT          ;  /* SFR STACK NEXT PAGE                           */

__sfr __at (0x86) SFRLAST          ;  /* SFR STACK LAST PAGE                           */

__sfr __at (0x87) PCON             ;  /* POWER CONTROL                                 */

__sfr __at (0x90) P1               ;  /* PORT 1                                        */

__sfr __at (0xA0) P2               ;  /* PORT 2                                        */

__sfr __at (0xA8) IE               ;  /* INTERRUPT ENABLE                              */

__sfr __at (0xB0) P3               ;  /* PORT 3                                        */

__sfr __at (0xB1) PSBANK           ;  /* FLASH BANK SELECT                             */

__sfr __at (0xB8) IP               ;  /* INTERRUPT PRIORITY                            */

__sfr __at (0xD0) PSW              ;  /* PROGRAM STATUS WORD                           */

__sfr __at (0xE0) ACC              ;  /* ACCUMULATOR                                   */

__sfr __at (0xE6) EIE1             ;  /* EXTERNAL INTERRUPT ENABLE 1                   */

__sfr __at (0xE7) EIE2             ;  /* EXTERNAL INTERRUPT ENABLE 2                   */

__sfr __at (0xF0) B                ;  /* B REGISTER                                    */

__sfr __at (0xF6) EIP1             ;  /* EXTERNAL INTERRUPT PRIORITY REGISTER 1        */

__sfr __at (0xF7) EIP2             ;  /* EXTERNAL INTERRUPT PRIORITY REGISTER 2        */

__sfr __at (0xFF) WDTCN            ;  /* WATCHDOG TIMER CONTROL                        */

/*  Page 0x00 */

__sfr __at (0x88) TCON             ;  /* TIMER CONTROL                                 */

__sfr __at (0x89) TMOD             ;  /* TIMER MODE                                    */

__sfr __at (0x8A) TL0              ;  /* TIMER 0 - LOW BYTE                            */

__sfr __at (0x8B) TL1              ;  /* TIMER 1 - LOW BYTE                            */

__sfr __at (0x8C) TH0              ;  /* TIMER 0 - HIGH BYTE                           */

__sfr __at (0x8D) TH1              ;  /* TIMER 1 - HIGH BYTE                           */

__sfr __at (0x8E) CKCON            ;  /* TIMER 0/1 CLOCK CONTROL                       */

__sfr __at (0x8F) PSCTL            ;  /* FLASH WRITE/ERASE CONTROL                     */

__sfr __at (0x91) SSTA0            ;  /* UART 0 STATUS                                 */

__sfr __at (0x98) SCON0            ;  /* UART 0 CONTROL                                */

__sfr __at (0x98) SCON             ;  /* UART 0 CONTROL                                */

__sfr __at (0x99) SBUF0            ;  /* UART 0 BUFFER                                 */

__sfr __at (0x99) SBUF             ;  /* UART 0 BUFFER                                 */

__sfr __at (0x9A) SPI0CFG          ;  /* SPI 0 CONFIGURATION                           */

__sfr __at (0x9B) SPI0DAT          ;  /* SPI 0 DATA                                    */

__sfr __at (0x9D) SPI0CKR          ;  /* SPI 0 CLOCK RATE CONTROL                      */

__sfr __at (0xA1) EMI0TC           ;  /* EMIF TIMING CONTROL                           */

__sfr __at (0xA2) EMI0CN           ;  /* EMIF CONTROL                                  */

__sfr __at (0xA2) _XPAGE           ;  /* XDATA/PDATA PAGE                              */

__sfr __at (0xA3) EMI0CF           ;  /* EMIF CONFIGURATION                            */

__sfr __at (0xA9) SADDR0           ;  /* UART 0 SLAVE ADDRESS                          */

__sfr __at (0xB7) FLSCL            ;  /* FLASH SCALE                                   */

__sfr __at (0xB9) SADEN0           ;  /* UART 0 SLAVE ADDRESS MASK                     */

__sfr __at (0xBA) AMX0CF           ;  /* ADC 0 MUX CONFIGURATION                       */

__sfr __at (0xBB) AMX0SL           ;  /* ADC 0 MUX CHANNEL SELECTION                   */

__sfr __at (0xBC) ADC0CF           ;  /* ADC 0 CONFIGURATION                           */

__sfr __at (0xBE) ADC0L            ;  /* ADC 0 DATA - LOW BYTE                         */

__sfr __at (0xBF) ADC0H            ;  /* ADC 0 DATA - HIGH BYTE                        */

__sfr __at (0xC0) SMB0CN           ;  /* SMBUS 0 CONTROL                               */

__sfr __at (0xC1) SMB0STA          ;  /* SMBUS 0 STATUS                                */

__sfr __at (0xC2) SMB0DAT          ;  /* SMBUS 0 DATA                                  */

__sfr __at (0xC3) SMB0ADR          ;  /* SMBUS 0 SLAVE ADDRESS                         */

__sfr __at (0xC4) ADC0GTL          ;  /* ADC 0 GREATER-THAN REGISTER - LOW BYTE        */

__sfr __at (0xC5) ADC0GTH          ;  /* ADC 0 GREATER-THAN REGISTER - HIGH BYTE       */

__sfr __at (0xC6) ADC0LTL          ;  /* ADC 0 LESS-THAN REGISTER - LOW BYTE           */

__sfr __at (0xC7) ADC0LTH          ;  /* ADC 0 LESS-THAN REGISTER - HIGH BYTE          */

__sfr __at (0xC8) TMR2CN           ;  /* TIMER 2 CONTROL                               */

__sfr __at (0xC9) TMR2CF           ;  /* TIMER 2 CONFIGURATION                         */

__sfr __at (0xCA) RCAP2L           ;  /* TIMER 2 CAPTURE REGISTER - LOW BYTE           */

__sfr __at (0xCB) RCAP2H           ;  /* TIMER 2 CAPTURE REGISTER - HIGH BYTE          */

__sfr __at (0xCC) TMR2L            ;  /* TIMER 2 - LOW BYTE                            */

__sfr __at (0xCC) TL2              ;  /* TIMER 2 - LOW BYTE                            */

__sfr __at (0xCD) TMR2H            ;  /* TIMER 2 - HIGH BYTE                           */

__sfr __at (0xCD) TH2              ;  /* TIMER 2 - HIGH BYTE                           */

__sfr __at (0xCF) SMB0CR           ;  /* SMBUS 0 CLOCK RATE                            */

__sfr __at (0xD1) REF0CN           ;  /* VOLTAGE REFERENCE 0 CONTROL                   */

__sfr __at (0xD2) DAC0L            ;  /* DAC 0 REGISTER - LOW BYTE                     */

__sfr __at (0xD3) DAC0H            ;  /* DAC 0 REGISTER - HIGH BYTE                    */

__sfr __at (0xD4) DAC0CN           ;  /* DAC 0 CONTROL                                 */

__sfr __at (0xD8) PCA0CN           ;  /* PCA 0 COUNTER CONTROL                         */

__sfr __at (0xD9) PCA0MD           ;  /* PCA 0 COUNTER MODE                            */

__sfr __at (0xDA) PCA0CPM0         ;  /* PCA 0 MODULE 0 CONTROL                        */

__sfr __at (0xDB) PCA0CPM1         ;  /* PCA 0 MODULE 1 CONTROL                        */

__sfr __at (0xDC) PCA0CPM2         ;  /* PCA 0 MODULE 2 CONTROL                        */

__sfr __at (0xDD) PCA0CPM3         ;  /* PCA 0 MODULE 3 CONTROL                        */

__sfr __at (0xDE) PCA0CPM4         ;  /* PCA 0 MODULE 4 CONTROL                        */

__sfr __at (0xDF) PCA0CPM5         ;  /* PCA 0 MODULE 5 CONTROL                        */

__sfr __at (0xE1) PCA0CPL5         ;  /* PCA 0 MODULE 5 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xE2) PCA0CPH5         ;  /* PCA 0 MODULE 5 CAPTURE/COMPARE - HIGH BYTE    */

__sfr __at (0xE8) ADC0CN           ;  /* ADC 0 CONTROL                                 */

__sfr __at (0xE9) PCA0CPL2         ;  /* PCA 0 MODULE 2 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xEA) PCA0CPH2         ;  /* PCA 0 MODULE 2 CAPTURE/COMPARE - HIGH BYTE    */

__sfr __at (0xEB) PCA0CPL3         ;  /* PCA 0 MODULE 3 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xEC) PCA0CPH3         ;  /* PCA 0 MODULE 3 CAPTURE/COMPARE - HIGH BYTE    */

__sfr __at (0xED) PCA0CPL4         ;  /* PCA 0 MODULE 4 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xEE) PCA0CPH4         ;  /* PCA 0 MODULE 4 CAPTURE/COMPARE - HIGH BYTE    */

__sfr __at (0xEF) RSTSRC           ;  /* RESET SOURCE                                  */

__sfr __at (0xF8) SPI0CN           ;  /* SPI 0 CONTROL                                 */

__sfr __at (0xF9) PCA0L            ;  /* PCA 0 TIMER - LOW BYTE                        */

__sfr __at (0xFA) PCA0H            ;  /* PCA 0 TIMER - HIGH BYTE                       */

__sfr __at (0xFB) PCA0CPL0         ;  /* PCA 0 MODULE 0 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xFC) PCA0CPH0         ;  /* PCA 0 MODULE 0 CAPTURE/COMPARE - HIGH BYTE    */

__sfr __at (0xFD) PCA0CPL1         ;  /* PCA 0 MODULE 1 CAPTURE/COMPARE - LOW BYTE     */

__sfr __at (0xFE) PCA0CPH1         ;  /* PCA 0 MODULE 1 CAPTURE/COMPARE - HIGH BYTE    */

/*  Page 0x01 */

__sfr __at (0x88) CPT0CN           ;  /* COMPARATOR 0 CONTROL                          */

__sfr __at (0x89) CPT0MD           ;  /* COMPARATOR 0 CONFIGURATION                    */

__sfr __at (0x98) SCON1            ;  /* UART 1 CONTROL                                */

__sfr __at (0x99) SBUF1            ;  /* UART 1 BUFFER                                 */

__sfr __at (0xC8) TMR3CN           ;  /* TIMER 3 CONTROL                               */

__sfr __at (0xC9) TMR3CF           ;  /* TIMER 3 CONFIGURATION                         */

__sfr __at (0xCA) RCAP3L           ;  /* TIMER 3 CAPTURE REGISTER - LOW BYTE           */

__sfr __at (0xCB) RCAP3H           ;  /* TIMER 3 CAPTURE REGISTER - HIGH BYTE          */

__sfr __at (0xCC) TMR3L            ;  /* TIMER 3 - LOW BYTE                            */

__sfr __at (0xCD) TMR3H            ;  /* TIMER 3 - HIGH BYTE                           */

__sfr __at (0xD2) DAC1L            ;  /* DAC 1 REGISTER - LOW BYTE                     */

__sfr __at (0xD3) DAC1H            ;  /* DAC 1 REGISTER - HIGH BYTE                    */

__sfr __at (0xD4) DAC1CN           ;  /* DAC 1 CONTROL                                 */

/*  Page 0x02 */

__sfr __at (0x88) CPT1CN           ;  /* COMPARATOR 1 CONTROL                          */

__sfr __at (0x89) CPT1MD           ;  /* COMPARATOR 1 CONFIGURATION                    */

__sfr __at (0xBA) AMX2CF           ;  /* ADC 2 MUX CONFIGURATION                       */

__sfr __at (0xBB) AMX2SL           ;  /* ADC 2 MUX CHANNEL SELECTION                   */

__sfr __at (0xBC) ADC2CF           ;  /* ADC 2 CONFIGURATION                           */

__sfr __at (0xBE) ADC2             ;  /* ADC 2 DATA                                    */

__sfr __at (0xC4) ADC2GT           ;  /* ADC 2 GREATER-THAN REGISTER                   */

__sfr __at (0xC6) ADC2LT           ;  /* ADC 2 LESS-THAN REGISTER                      */

__sfr __at (0xC8) TMR4CN           ;  /* TIMER 4 CONTROL                               */

__sfr __at (0xC9) TMR4CF           ;  /* TIMER 4 CONFIGURATION                         */

__sfr __at (0xCA) RCAP4L           ;  /* TIMER 4 CAPTURE REGISTER - LOW BYTE           */

__sfr __at (0xCB) RCAP4H           ;  /* TIMER 4 CAPTURE REGISTER - HIGH BYTE          */

__sfr __at (0xCC) TMR4L            ;  /* TIMER 4 - LOW BYTE                            */

__sfr __at (0xCD) TMR4H            ;  /* TIMER 4 - HIGH BYTE                           */

__sfr __at (0xE8) ADC2CN           ;  /* ADC 2 CONTROL                                 */

/*  Page 0x03 */

__sfr __at (0x91) MAC0BL           ;  /* MAC0 B Register Low Byte                      */

__sfr __at (0x92) MAC0BH           ;  /* MAC0 B Register High Byte                     */

__sfr __at (0x93) MAC0ACC0         ;  /* MAC0 Accumulator Byte 0 (LSB)                 */

__sfr __at (0x94) MAC0ACC1         ;  /* MAC0 Accumulator Byte 1                       */

__sfr __at (0x95) MAC0ACC2         ;  /* MAC0 Accumulator Byte 2                       */

__sfr __at (0x96) MAC0ACC3         ;  /* MAC0 Accumulator Byte 3 (MSB)                 */

__sfr __at (0x97) MAC0OVR          ;  /* MAC0 Accumulator Overflow                     */

__sfr __at (0xC0) MAC0STA          ;  /* MAC0 Status Register                          */

__sfr __at (0xC1) MAC0AL           ;  /* MAC0 A Register Low Byte                      */

__sfr __at (0xC2) MAC0AH           ;  /* MAC0 A Register High Byte                     */

__sfr __at (0xC3) MAC0CF           ;  /* MAC0 Configuration                            */

__sfr __at (0xCE) MAC0RNDL         ;  /* MAC0 Rounding Register Low Byte               */

__sfr __at (0xCF) MAC0RNDH         ;  /* MAC0 Rounding Register High Byte              */

/*  Page 0x0F */

__sfr __at (0x88) FLSTAT           ;  /* FLASH STATUS                                  */

__sfr __at (0x89) PLL0CN           ;  /* PLL 0 CONTROL                                 */

__sfr __at (0x8A) OSCICN           ;  /* INTERNAL OSCILLATOR CONTROL                   */

__sfr __at (0x8B) OSCICL           ;  /* INTERNAL OSCILLATOR CALIBRATION               */

__sfr __at (0x8C) OSCXCN           ;  /* EXTERNAL OSCILLATOR CONTROL                   */

__sfr __at (0x8D) PLL0DIV          ;  /* PLL 0 DIVIDER                                 */

__sfr __at (0x8E) PLL0MUL          ;  /* PLL 0 MULTIPLIER                              */

__sfr __at (0x8F) PLL0FLT          ;  /* PLL 0 FILTER                                  */

__sfr __at (0x96) SFRPGCN          ;  /* SFR PAGE CONTROL                              */

__sfr __at (0x97) CLKSEL           ;  /* SYSTEM CLOCK SELECT                           */

__sfr __at (0x9A) CCH0MA           ;  /* CACHE MISS ACCUMULATOR                        */

__sfr __at (0x9C) P4MDOUT          ;  /* PORT 4 OUTPUT MODE                            */

__sfr __at (0x9D) P5MDOUT          ;  /* PORT 5 OUTPUT MODE                            */

__sfr __at (0x9E) P6MDOUT          ;  /* PORT 6 OUTPUT MODE                            */

__sfr __at (0x9F) P7MDOUT          ;  /* PORT 7 OUTPUT MODE                            */

__sfr __at (0xA1) CCH0CN           ;  /* CACHE CONTROL                                 */

__sfr __at (0xA2) CCH0TN           ;  /* CACHE TUNING REGISTER                         */

__sfr __at (0xA3) CCH0LC           ;  /* CACHE LOCK                                    */

__sfr __at (0xA4) P0MDOUT          ;  /* PORT 0 OUTPUT MODE                            */

__sfr __at (0xA5) P1MDOUT          ;  /* PORT 1 OUTPUT MODE                            */

__sfr __at (0xA6) P2MDOUT          ;  /* PORT 2 OUTPUT MODE CONFIGURATION              */

__sfr __at (0xA7) P3MDOUT          ;  /* PORT 3 OUTPUT MODE CONFIGURATION              */

__sfr __at (0xAD) P1MDIN           ;  /* PORT 1 INPUT MODE                             */

__sfr __at (0xB7) FLACL            ;  /* FLASH ACCESS LIMIT                            */

__sfr __at (0xC8) P4               ;  /* PORT 4                                        */

__sfr __at (0xD8) P5               ;  /* PORT 5                                        */

__sfr __at (0xE1) XBR0             ;  /* CROSSBAR CONFIGURATION REGISTER 0             */

__sfr __at (0xE2) XBR1             ;  /* CROSSBAR CONFIGURATION REGISTER 1             */

__sfr __at (0xE3) XBR2             ;  /* CROSSBAR CONFIGURATION REGISTER 2             */

__sfr __at (0xE8) P6               ;  /* PORT 6                                        */

__sfr __at (0xF8) P7               ;  /* PORT 7                                        */

/*  WORD/DWORD Registers  */

/*  Page 0x00 */

__sfr16 __at (0x8C8A) TMR0         ;  /* TIMER 0 COUNTER                               */

__sfr16 __at (0x8D8B) TMR1         ;  /* TIMER 1 COUNTER                               */

__sfr16 __at (0xCDCC) TMR2         ;  /* TIMER 2 COUNTER                               */

__sfr16 __at (0xCBCA) RCAP2        ;  /* TIMER 2 CAPTURE REGISTER WORD                 */

__sfr16 __at (0xBFBE) ADC0         ;  /* ADC 0 DATA WORD                               */

__sfr16 __at (0xC5C4) ADC0GT       ;  /* ADC 0 GREATER-THAN REGISTER WORD              */

__sfr16 __at (0xC7C6) ADC0LT       ;  /* ADC 0 LESS-THAN REGISTER WORD                 */

__sfr16 __at (0xD3D2) DAC0         ;  /* DAC 0 REGISTER WORD                           */

__sfr16 __at (0xFAF9) PCA0         ;  /* PCA 0 TIMER COUNTER                           */

__sfr16 __at (0xFCFB) PCA0CP0      ;  /* PCA 0 MODULE 0 CAPTURE/COMPARE WORD           */

__sfr16 __at (0xFEFD) PCA0CP1      ;  /* PCA 0 MODULE 1 CAPTURE/COMPARE WORD           */

__sfr16 __at (0xEAE9) PCA0CP2      ;  /* PCA 0 MODULE 2 CAPTURE/COMPARE WORD           */

__sfr16 __at (0xECEB) PCA0CP3      ;  /* PCA 0 MODULE 3 CAPTURE/COMPARE WORD           */

__sfr16 __at (0xEEED) PCA0CP4      ;  /* PCA 0 MODULE 4 CAPTURE/COMPARE WORD           */

__sfr16 __at (0xE2E1) PCA0CP5      ;  /* PCA 0 MODULE 5 CAPTURE/COMPARE WORD           */

/*  Page 0x01 */

__sfr16 __at (0xCDCC) TMR3         ;  /* TIMER 3 COUNTER                               */

__sfr16 __at (0xCBCA) RCAP3        ;  /* TIMER 3 CAPTURE REGISTER WORD                 */

__sfr16 __at (0xD3D2) DAC1         ;  /* DAC 1 REGISTER WORD                           */

/*  Page 0x02 */

__sfr16 __at (0xCDCC) TMR4         ;  /* TIMER 4 COUNTER                               */

__sfr16 __at (0xCBCA) RCAP4        ;  /* TIMER 4 CAPTURE REGISTER WORD                 */

/*  Page 0x03 */

__sfr16 __at (0xC2C1) MAC0A        ;  /* MAC0 A Register                               */

/* No sfr16 definition for MAC0B because MAC0BL must be written last */

__sfr32 __at (0x96959493) MAC0ACC  ;  /* MAC0 Accumulator                              */

__sfr16 __at (0xCFCE) MAC0RND      ;  /* MAC0 Rounding Register                        */

/*  BIT Registers  */

/*  P0  0x80 */

__sbit __at (0x80) P0_0            ;

__sbit __at (0x81) P0_1            ;

__sbit __at (0x82) P0_2            ;

__sbit __at (0x83) P0_3            ;

__sbit __at (0x84) P0_4            ;

__sbit __at (0x85) P0_5            ;

__sbit __at (0x86) P0_6            ;

__sbit __at (0x87) P0_7            ;

/*  TCON  0x88 */

__sbit __at (0x88) IT0             ;  /* EXT. INTERRUPT 0 TYPE                         */

__sbit __at (0x89) IE0             ;  /* EXT. INTERRUPT 0 EDGE FLAG                    */

__sbit __at (0x8A) IT1             ;  /* EXT. INTERRUPT 1 TYPE                         */

__sbit __at (0x8B) IE1             ;  /* EXT. INTERRUPT 1 EDGE FLAG                    */

__sbit __at (0x8C) TR0             ;  /* TIMER 0 ON/OFF CONTROL                        */

__sbit __at (0x8D) TF0             ;  /* TIMER 0 OVERFLOW FLAG                         */

__sbit __at (0x8E) TR1             ;  /* TIMER 1 ON/OFF CONTROL                        */

__sbit __at (0x8F) TF1             ;  /* TIMER 1 OVERFLOW FLAG                         */

/*  CPT0CN  0x88 */

__sbit __at (0x88) CP0HYN0         ;  /* COMPARATOR 0 NEGATIVE HYSTERESIS 0            */

__sbit __at (0x89) CP0HYN1         ;  /* COMPARATOR 0 NEGATIVE HYSTERESIS 1            */

__sbit __at (0x8A) CP0HYP0         ;  /* COMPARATOR 0 POSITIVE HYSTERESIS 0            */

__sbit __at (0x8B) CP0HYP1         ;  /* COMPARATOR 0 POSITIVE HYSTERESIS 1            */

__sbit __at (0x8C) CP0FIF          ;  /* COMPARATOR 0 FALLING EDGE INTERRUPT           */

__sbit __at (0x8D) CP0RIF          ;  /* COMPARATOR 0 RISING EDGE INTERRUPT            */

__sbit __at (0x8E) CP0OUT          ;  /* COMPARATOR 0 OUTPUT                           */

__sbit __at (0x8F) CP0EN           ;  /* COMPARATOR 0 ENABLE                           */

/*  CPT1CN  0x88 */

__sbit __at (0x88) CP1HYN0         ;  /* COMPARATOR 1 NEGATIVE HYSTERESIS 0            */

__sbit __at (0x89) CP1HYN1         ;  /* COMPARATOR 1 NEGATIVE HYSTERESIS 1            */

__sbit __at (0x8A) CP1HYP0         ;  /* COMPARATOR 1 POSITIVE HYSTERESIS 0            */

__sbit __at (0x8B) CP1HYP1         ;  /* COMPARATOR 1 POSITIVE HYSTERESIS 1            */

__sbit __at (0x8C) CP1FIF          ;  /* COMPARATOR 1 FALLING EDGE INTERRUPT           */

__sbit __at (0x8D) CP1RIF          ;  /* COMPARATOR 1 RISING EDGE INTERRUPT            */

__sbit __at (0x8E) CP1OUT          ;  /* COMPARATOR 1 OUTPUT                           */

__sbit __at (0x8F) CP1EN           ;  /* COMPARATOR 1 ENABLE                           */

/*  FLSTAT  0x88 */

__sbit __at (0x88) FLHBUSY         ;  /* FLASH BUSY                                    */

/*  P1  0x90 */

__sbit __at (0x90) P1_0            ;

__sbit __at (0x91) P1_1            ;

__sbit __at (0x92) P1_2            ;

__sbit __at (0x93) P1_3            ;

__sbit __at (0x94) P1_4            ;

__sbit __at (0x95) P1_5            ;

__sbit __at (0x96) P1_6            ;

__sbit __at (0x97) P1_7            ;

/*  SCON0  0x98 */

__sbit __at (0x98) RI0             ;  /* UART 0 RX INTERRUPT FLAG                      */

__sbit __at (0x98) RI              ;  /* UART 0 RX INTERRUPT FLAG                      */

__sbit __at (0x99) TI0             ;  /* UART 0 TX INTERRUPT FLAG                      */

__sbit __at (0x99) TI              ;  /* UART 0 TX INTERRUPT FLAG                      */

__sbit __at (0x9A) RB80            ;  /* UART 0 RX BIT 8                               */

__sbit __at (0x9B) TB80            ;  /* UART 0 TX BIT 8                               */

__sbit __at (0x9C) REN0            ;  /* UART 0 RX ENABLE                              */

__sbit __at (0x9C) REN             ;  /* UART 0 RX ENABLE                              */

__sbit __at (0x9D) SM20            ;  /* UART 0 MULTIPROCESSOR EN                      */

__sbit __at (0x9E) SM10            ;  /* UART 0 MODE 1                                 */

__sbit __at (0x9F) SM00            ;  /* UART 0 MODE 0                                 */

/*  SCON1  0x98 */

__sbit __at (0x98) RI1             ;  /* UART 1 RX INTERRUPT FLAG                      */

__sbit __at (0x99) TI1             ;  /* UART 1 TX INTERRUPT FLAG                      */

__sbit __at (0x9A) RB81            ;  /* UART 1 RX BIT 8                               */

__sbit __at (0x9B) TB81            ;  /* UART 1 TX BIT 8                               */

__sbit __at (0x9C) REN1            ;  /* UART 1 RX ENABLE                              */

__sbit __at (0x9D) MCE1            ;  /* UART 1 MCE                                    */

__sbit __at (0x9F) S1MODE          ;  /* UART 1 MODE                                   */

/*  P2  0xA0 */

__sbit __at (0xA0) P2_0            ;

__sbit __at (0xA1) P2_1            ;

__sbit __at (0xA2) P2_2            ;

__sbit __at (0xA3) P2_3            ;

__sbit __at (0xA4) P2_4            ;

__sbit __at (0xA5) P2_5            ;

__sbit __at (0xA6) P2_6            ;

__sbit __at (0xA7) P2_7            ;

/*  IE  0xA8 */

__sbit __at (0xA8) EX0             ;  /* EXTERNAL INTERRUPT 0 ENABLE                   */

__sbit __at (0xA9) ET0             ;  /* TIMER 0 INTERRUPT ENABLE                      */

__sbit __at (0xAA) EX1             ;  /* EXTERNAL INTERRUPT 1 ENABLE                   */

__sbit __at (0xAB) ET1             ;  /* TIMER 1 INTERRUPT ENABLE                      */

__sbit __at (0xAC) ES0             ;  /* UART0 INTERRUPT ENABLE                        */

__sbit __at (0xAC) ES              ;  /* UART0 INTERRUPT ENABLE                        */

__sbit __at (0xAD) ET2             ;  /* TIMER 2 INTERRUPT ENABLE                      */

__sbit __at (0xAF) EA              ;  /* GLOBAL INTERRUPT ENABLE                       */

/*  P3  0xB0 */

__sbit __at (0xB0) P3_0            ;

__sbit __at (0xB1) P3_1            ;

__sbit __at (0xB2) P3_2            ;

__sbit __at (0xB3) P3_3            ;

__sbit __at (0xB4) P3_4            ;

__sbit __at (0xB5) P3_5            ;

__sbit __at (0xB6) P3_6            ;

__sbit __at (0xB7) P3_7            ;

/*  IP  0xB8 */

__sbit __at (0xB8) PX0             ;  /* EXTERNAL INTERRUPT 0 PRIORITY                 */

__sbit __at (0xB9) PT0             ;  /* TIMER 0 PRIORITY                              */

__sbit __at (0xBA) PX1             ;  /* EXTERNAL INTERRUPT 1 PRIORITY                 */

__sbit __at (0xBB) PT1             ;  /* TIMER 1 PRIORITY                              */

__sbit __at (0xBC) PS0             ;  /* SERIAL PORT PRIORITY                          */

__sbit __at (0xBC) PS              ;  /* SERIAL PORT PRIORITY                          */

__sbit __at (0xBD) PT2             ;  /* TIMER 2 PRIORITY                              */

/* SMB0CN 0xC0 */

__sbit __at (0xC0) SMBTOE          ;  /* SMBUS 0 TIMEOUT ENABLE                        */

__sbit __at (0xC1) SMBFTE          ;  /* SMBUS 0 FREE TIMER ENABLE                     */

__sbit __at (0xC2) AA              ;  /* SMBUS 0 ASSERT/ACKNOWLEDGE FLAG               */

__sbit __at (0xC3) SI              ;  /* SMBUS 0 INTERRUPT PENDING FLAG                */

__sbit __at (0xC4) STO             ;  /* SMBUS 0 STOP FLAG                             */

__sbit __at (0xC5) STA             ;  /* SMBUS 0 START FLAG                            */

__sbit __at (0xC6) ENSMB           ;  /* SMBUS 0 ENABLE                                */

__sbit __at (0xC7) BUSY            ;  /* SMBUS 0 BUSY                                  */

/* MAC0STA 0xC0 */

__sbit __at (0xC0) MAC0N           ;  /* MAC 0 NEGATIVE FLAG                           */

__sbit __at (0xC1) MAC0SO          ;  /* MAC 0 SOFT OVERFLOW FLAG                      */

__sbit __at (0xC2) MAC0Z           ;  /* MAC 0 ZERO FLAG                               */

__sbit __at (0xC3) MAC0HO          ;  /* MAC 0 HARD OVERFLOW FLAG                      */

/*  TMR2CN  0xC8 */

__sbit __at (0xC8) CPRL2           ;  /* TIMER 2 CAPTURE SELECT                        */

__sbit __at (0xC9) CT2             ;  /* TIMER 2 COUNTER SELECT                        */

__sbit __at (0xCA) TR2             ;  /* TIMER 2 ON/OFF CONTROL                        */

__sbit __at (0xCB) EXEN2           ;  /* TIMER 2 EXTERNAL ENABLE FLAG                  */

__sbit __at (0xCE) EXF2            ;  /* TIMER 2 EXTERNAL FLAG                         */

__sbit __at (0xCF) TF2             ;  /* TIMER 2 OVERFLOW FLAG                         */

/*  TMR3CN  0xC8 */

__sbit __at (0xC8) CPRL3           ;  /* TIMER 3 CAPTURE SELECT                        */

__sbit __at (0xC9) CT3             ;  /* TIMER 3 COUNTER SELECT                        */

__sbit __at (0xCA) TR3             ;  /* TIMER 3 ON/OFF CONTROL                        */

__sbit __at (0xCB) EXEN3           ;  /* TIMER 3 EXTERNAL ENABLE FLAG                  */

__sbit __at (0xCE) EXF3            ;  /* TIMER 3 EXTERNAL FLAG                         */

__sbit __at (0xCF) TF3             ;  /* TIMER 3 OVERFLOW FLAG                         */

/*  TMR4CN  0xC8 */

__sbit __at (0xC8) CPRL4           ;  /* TIMER 4 CAPTURE SELECT                        */

__sbit __at (0xC9) CT4             ;  /* TIMER 4 COUNTER SELECT                        */

__sbit __at (0xCA) TR4             ;  /* TIMER 4 ON/OFF CONTROL                        */

__sbit __at (0xCB) EXEN4           ;  /* TIMER 4 EXTERNAL ENABLE FLAG                  */

__sbit __at (0xCE) EXF4            ;  /* TIMER 4 EXTERNAL FLAG                         */

__sbit __at (0xCF) TF4             ;  /* TIMER 4 OVERFLOW FLAG                         */

/*  P4  0xC8 */

__sbit __at (0xC8) P4_0            ;

__sbit __at (0xC9) P4_1            ;

__sbit __at (0xCA) P4_2            ;

__sbit __at (0xCB) P4_3            ;

__sbit __at (0xCC) P4_4            ;

__sbit __at (0xCD) P4_5            ;

__sbit __at (0xCE) P4_6            ;

__sbit __at (0xCF) P4_7            ;

/*  PSW  0xD0 */

__sbit __at (0xD0) P               ;  /* ACCUMULATOR PARITY FLAG                       */

__sbit __at (0xD1) F1              ;  /* USER FLAG 1                                   */

__sbit __at (0xD2) OV              ;  /* OVERFLOW FLAG                                 */

__sbit __at (0xD3) RS0             ;  /* REGISTER BANK SELECT 0                        */

__sbit __at (0xD4) RS1             ;  /* REGISTER BANK SELECT 1                        */

__sbit __at (0xD5) F0              ;  /* USER FLAG 0                                   */

__sbit __at (0xD6) AC              ;  /* AUXILIARY CARRY FLAG                          */

__sbit __at (0xD7) CY              ;  /* CARRY FLAG                                    */

/* PCA0CN D8H */

__sbit __at (0xD8) CCF0            ;  /* PCA 0 MODULE 0 INTERRUPT FLAG                 */

__sbit __at (0xD9) CCF1            ;  /* PCA 0 MODULE 1 INTERRUPT FLAG                 */

__sbit __at (0xDA) CCF2            ;  /* PCA 0 MODULE 2 INTERRUPT FLAG                 */

__sbit __at (0xDB) CCF3            ;  /* PCA 0 MODULE 3 INTERRUPT FLAG                 */

__sbit __at (0xDC) CCF4            ;  /* PCA 0 MODULE 4 INTERRUPT FLAG                 */

__sbit __at (0xDD) CCF5            ;  /* PCA 0 MODULE 5 INTERRUPT FLAG                 */

__sbit __at (0xDE) CR              ;  /* PCA 0 COUNTER RUN CONTROL BIT                 */

__sbit __at (0xDF) CF              ;  /* PCA 0 COUNTER OVERFLOW FLAG                   */

/*  P5  0xD8 */

__sbit __at (0xD8) P5_0            ;

__sbit __at (0xD9) P5_1            ;

__sbit __at (0xDA) P5_2            ;

__sbit __at (0xDB) P5_3            ;

__sbit __at (0xDC) P5_4            ;

__sbit __at (0xDD) P5_5            ;

__sbit __at (0xDE) P5_6            ;

__sbit __at (0xDF) P5_7            ;

/* ADC0CN E8H */

__sbit __at (0xE8) AD0LJST         ;  /* ADC 0 RIGHT JUSTIFY DATA BIT                  */

__sbit __at (0xE9) AD0WINT         ;  /* ADC 0 WINDOW INTERRUPT FLAG                   */

__sbit __at (0xEA) AD0CM0          ;  /* ADC 0 CONVERT START MODE BIT 0                */

__sbit __at (0xEB) AD0CM1          ;  /* ADC 0 CONVERT START MODE BIT 1                */

__sbit __at (0xEC) AD0BUSY         ;  /* ADC 0 BUSY FLAG                               */

__sbit __at (0xED) AD0INT          ;  /* ADC 0 EOC INTERRUPT FLAG                      */

__sbit __at (0xEE) AD0TM           ;  /* ADC 0 TRACK MODE                              */

__sbit __at (0xEF) AD0EN           ;  /* ADC 0 ENABLE                                  */

/* ADC2CN E8H */

__sbit __at (0xE8) AD2WINT         ;  /* ADC 2 WINDOW INTERRUPT FLAG                   */

__sbit __at (0xE9) AD2CM0          ;  /* ADC 2 CONVERT START MODE BIT 0                */

__sbit __at (0xEA) AD2CM1          ;  /* ADC 2 CONVERT START MODE BIT 1                */

__sbit __at (0xEB) AD2CM2          ;  /* ADC 2 CONVERT START MODE BIT 2                */

__sbit __at (0xEC) AD2BUSY         ;  /* ADC 2 BUSY FLAG                               */

__sbit __at (0xED) AD2INT          ;  /* ADC 2 EOC INTERRUPT FLAG                      */

__sbit __at (0xEE) AD2TM           ;  /* ADC 2 TRACK MODE                              */

__sbit __at (0xEF) AD2EN           ;  /* ADC 2 ENABLE                                  */

/*  P6  0xE8 */

__sbit __at (0xE8) P6_0            ;

__sbit __at (0xE9) P6_1            ;

__sbit __at (0xEA) P6_2            ;

__sbit __at (0xEB) P6_3            ;

__sbit __at (0xEC) P6_4            ;

__sbit __at (0xED) P6_5            ;

__sbit __at (0xEE) P6_6            ;

__sbit __at (0xEF) P6_7            ;

/* SPI0CN F8H */

__sbit __at (0xF8) SPIEN           ;  /* SPI 0 SPI ENABLE                              */

__sbit __at (0xF9) TXBMT           ;  /* SPI 0 TX BUFFER EMPTY FLAG                    */

__sbit __at (0xFA) NSSMD0          ;  /* SPI 0 SLAVE SELECT MODE 0                     */

__sbit __at (0xFB) NSSMD1          ;  /* SPI 0 SLAVE SELECT MODE 1                     */

__sbit __at (0xFC) RXOVRN          ;  /* SPI 0 RX OVERRUN FLAG                         */

__sbit __at (0xFD) MODF            ;  /* SPI 0 MODE FAULT FLAG                         */

__sbit __at (0xFE) WCOL            ;  /* SPI 0 WRITE COLLISION FLAG                    */

__sbit __at (0xFF) SPIF            ;  /* SPI 0 INTERRUPT FLAG                          */

/*  P7  0xF8 */

__sbit __at (0xF8) P7_0            ;

__sbit __at (0xF9) P7_1            ;

__sbit __at (0xFA) P7_2            ;

__sbit __at (0xFB) P7_3            ;

__sbit __at (0xFC) P7_4            ;

__sbit __at (0xFD) P7_5            ;

__sbit __at (0xFE) P7_6            ;

__sbit __at (0xFF) P7_7            ;

/* Predefined SFR Bit Masks */

#define PCON_IDLE         0x01    /* PCON                                */

#define PCON_STOP         0x02    /* PCON                                */

#define ECCF              0x01    /* PCA0CPMn                            */

#define PWM               0x02    /* PCA0CPMn                            */

#define TOG               0x04    /* PCA0CPMn                            */

#define MAT               0x08    /* PCA0CPMn                            */

#define CAPN              0x10    /* PCA0CPMn                            */

#define CAPP              0x20    /* PCA0CPMn                            */

#define ECOM              0x40    /* PCA0CPMn                            */

#define PWM16             0x80    /* PCA0CPMn                            */

#define PINRSF            0x01    /* RSTSRC                              */

#define PORSF             0x02    /* RSTSRC                              */

#define MCDRSF            0x04    /* RSTSRC                              */

#define WDTRSF            0x08    /* RSTSRC                              */

#define SWRSF             0x10    /* RSTSRC                              */

#define C0RSEF            0x20    /* RSTSRC                              */

#define CNVRSEF           0x40    /* RSTSRC                              */

/* SFR PAGE DEFINITIONS */

#define CONFIG_PAGE       0x0F     /* SYSTEM AND PORT CONFIGURATION PAGE */

#define LEGACY_PAGE       0x00     /* LEGACY SFR PAGE                    */

#define TIMER01_PAGE      0x00     /* TIMER 0 AND TIMER 1                */

#define CPT0_PAGE         0x01     /* COMPARATOR 0                       */

#define CPT1_PAGE         0x02     /* COMPARATOR 1                       */

#define UART0_PAGE        0x00     /* UART 0                             */

#define UART1_PAGE        0x01     /* UART 1                             */

#define SPI0_PAGE         0x00     /* SPI 0                              */

#define EMI0_PAGE         0x00     /* EXTERNAL MEMORY INTERFACE          */

#define ADC0_PAGE         0x00     /* ADC 0                              */

#define ADC2_PAGE         0x02     /* ADC 2                              */

#define SMB0_PAGE         0x00     /* SMBUS 0                            */

#define TMR2_PAGE         0x00     /* TIMER 2                            */

#define TMR3_PAGE         0x01     /* TIMER 3                            */

#define TMR4_PAGE         0x02     /* TIMER 4                            */

#define DAC0_PAGE         0x00     /* DAC 0                              */

#define DAC1_PAGE         0x01     /* DAC 1                              */

#define PCA0_PAGE         0x00     /* PCA 0                              */

#define PLL0_PAGE         0x0F     /* PLL 0                              */

#define MAC0_PAGE         0x03     /* MULTIPLY / ACCUMULATE 0            */

#endif

libdoc.txt – MATH FUNCTION LIST

Not finished - 20 Jan 2002 - checkpoint (Steve Kenton)

This is a sorted (ignoring leading '_') list of the SDCC library.

Sources are in ~sdcc/device/lib/*.c and ~sdcc/device/include/*.h.

Except where denoted with MACRO these are implemented as functions.

Internal function calls are generated by the compiler to implement

IEEE floating point, etc.  They are not normally called directly.

isalnum - character classification - #include <ctype.h> - all ports

char isalnum (unsigned char c); MACRO

Return true if c is an ASCII letter or digit

'a-z','A-Z', '0'-'9' otherwise return false.

isalpha - character classification - #include <ctype.h> - all ports

char isalpha (unsigned char c); MACRO

Return true if c is an ASCII letter

'a-z','A-Z' otherwise return false.

isascii - character classification - #include <ctype.h> - missing

char isascii (unsigned char c);

Return true if c is an 7-bit ASCII character

0x00-0x7F otherwise return false.

iscntrl - character classification - #include <ctype.h> - all ports

char iscntrl (unsigned char c);

Return true if c is an ASCII control character

0x00-0x1F or 0x7F (DEL) otherwise return false.

isdigit - character classification - #include <ctype.h> - all ports

char isdigit (unsigned char c);

Return true if c is an ASCII digit '0'-'9'

otherwise return false.

isgraph - character classification - #include <ctype.h> - all ports

char isgraph (unsigned char c);

Return true is c is an ASCII printable graphic

excluding space 0x21-0x7E otherwise return false.

islower - character classification - #include <ctype.h> - all ports

char islower (unsigned char c);

Return true if c is an ASCII lower case letter

'a'-'z' otherwise return false.

isprint - character classification - #include <ctype.h> - all ports

char isprint (unsigned char c);

Return true is c is an ASCII printable graphic

including space 0x20-0x7E otherwise return false.

ispunct - character classification - #include <ctype.h> - all ports

char ispunct (unsigned char c);

Return true if c is ASCII punctuation (isgraph but not isalnum)

otherwise return false.

isspace - character classification - #include <ctype.h> - all ports

char isspace (unsigned char c);

Return true if c is an ASCII white space character

space, tab, carriage return, newline or vertical tab

0x09-0x0D, 0x20 otherwise return false.

isupper - character classification - #include <ctype.h> - all ports

char isupper (unsigned char c);

Return true if c is an ASCII upper case letter

'A'-'Z' otherwise return false.

isxdigit - character classification - #include <ctype.h> - all ports

char isxdigit (unsigned char c);

Return true if c is an ASCII hexidecimal digit

'0-9','a-f','A-F' otherwise return false.

toascii - character classification - #include <ctype.h> - all ports

char toascii(unsigned char c); MACRO

Convert c from 8-bit value to 7-bit ASCII.

tolower - character classification - #include <ctype.h> - all ports

char _tolower(unsigned char c); MACRO

char tolower(unsigned char c); MACRO

Convert c from upper case to lower case.

toupper - character classification - #include <ctype.h> - all ports

char _toupper(unsigned char c); MACRO

char toupper(unsigned char c); MACRO

Convert c from lower case to upper case.

__uchar2fs - IEEE single precision math - #include <float.h> - ??? ports

float __uchar2fs (unsigned char uc); INTERNAL

Convert an unsigned char to float.

__schar2fs - IEEE single precision math - #include <float.h> - ??? ports

float __schar2fs (signed char sc); INTERNAL

Convert a signed char to float.

__uint2fs - IEEE single precision math - #include <float.h> - ??? ports

float __uint2fs (unsigned int ui); INTERNAL

Convert an unsigned int to float.

__sint2fs - IEEE single precision math - #include <float.h> - ??? ports

float __sint2fs (signed int si); INTERNAL

Convert a signed int to float.

__ulong2fs - IEEE single precision math - #include <float.h> - ??? ports

float __ulong2fs (unsigned long ul); INTERNAL

Convert an unsigned log to float.

__slong2fs - IEEE single precision math - #include <float.h> - ??? ports

float __slong2fs (signed long sl); INTERNAL

Convert a signed long to float.

__fs2uchar - IEEE single precision math - #include <float.h> - ??? ports

unsigned char __fs2uchar (float f); INTERNAL

Convert a float to unsigned char;

__fs2schar - IEEE single precision math - #include <float.h> - ??? ports

signed char __fs2schar (float f); INTERNAL

Convert a float to signed char;

__fs2uint - IEEE single precision math - #include <float.h> - ??? ports

unsigned int __fs2uint (float f); INTERNAL

Convert a float to unsigned int;

__fs2sint - IEEE single precision math - #include <float.h> - ??? ports

signed int __fs2sint (float f); INTERNAL

Convert a float to signed int;

__fs2ulong - IEEE single precision math - #include <float.h> - ??? ports

unsigned long __fs2ulong (float f); INTERNAL

Convert a float to unsigned long;

__fs2slong - IEEE single precision math - #include <float.h> - ??? ports

signed long __fs2slong (float f); INTERNAL

Convert a float to signed long.

__fsadd - IEEE single precision math - #include <float.h> - ??? ports

float __fsadd (float a1, float a2); INTERNAL

Add two floats.

__fssub - IEEE single precision math - #include <float.h> - ??? ports

float __fssub (float a1, float a2); INTERNAL

Subtract two floats.

__fsmul - IEEE single precision math - #include <float.h> - ??? ports

float __fsmul (float a1, float a2); INTERNAL

Multiply two floats.

__fsdiv - IEEE single precision math - #include <float.h> - ??? ports

float __fsdiv (float a1, float a2); INTERNAL

Divide two floats.

__fslt - IEEE single precision math - #include <float.h> - ??? ports

char __fslt (float a1, float a2); INTERNAL

Compare two floats lt.

__fseq - IEEE single precision math - #include <float.h> - ??? ports

char __fseq (float a1, float a2); INTERNAL

Compare two floats eq.

__fsneq - IEEE single precision math - #include <float.h> - ??? ports

char __fseq (float a1, float a2); INTERNAL ??? missing in float.h ???

Compare two floats neq.

__fsgt - IEEE single precision math - #include <float.h> - ??? ports

char __fsgt (float a1, float a2); INTERNAL ??? typo in float.h ???

Compare two floats gt.

malloc - memory allocation - #include <malloc.h> - ??? ports

void *malloc (unsigned int);

void xdata * malloc (unsigned int );

Allocate a block of memory from the heap;

free - memory allocation - #include <malloc.h> - ??? ports

void free (void *p);

void free (void xdata *  p);

Return previously allocated memory to the heap.

init_dynamic_memory - memory allocation - #include <malloc.h> - ??? ports

void init_dynamic_memory (MEMHEADER xdata *  , unsigned int );

Initialize the memory allocation system.

sincosf - ANSI C math - #include <math.h> - all ports

float sincosf(const float x, const int iscos); INTERNAL

Compute the sine or cosine of x.

tancotf - ANSI C math - #include <math.h> - all ports

float tancotf(const float x, const int iscot); INTERNAL

Compute the tangent or cotangent of x.

asincosf - ANSI C math - #include <math.h> - all ports

float asincosf(const float x, const int isacos); INTERNAL

Compute the arc sine or arc cosine of x.

sincoshf - ANSI C math - #include <math.h> - all ports

float sincoshf(const float x, const int iscosh); INTERNAL

Compute the hyperbolic sine or hyperbolic cosine of x.

sinf - ANSI C math - #include <math.h> - all ports

float sinf (const float x);

Compute sine of x.

cosf - ANSI C math - #include <math.h> - all ports

float cosf (const float x);

Compute cosine of x.

tanf - ANSI C math - #include <math.h> - all ports

float tanf (const float x);

Compute tangent of x.

cotf - ANSI C math - #include <math.h> - all ports

float cotf (const float x);

Compute cotangent of x.

asinf - ANSI C math - #include <math.h> - all ports

float asinf (const float x);

Compute the arc sine of x.

acosf - ANSI C math - #include <math.h> - all ports

float acosf (const float x);

Compute the arc cosine of x.

atanf - ANSI C math - #include <math.h> - all ports

float atanf (const float x);

Compute the arc tangent of x.

atan2f - ANSI C math - #include <math.h> - all ports

float atan2f (const float x, const float y); ??? x,y reversed ???

Compute the arc tangent of (x/y);

sinhf - ANSI C math - #include <math.h> - all ports

float sinhf (const float x);

Compute the hyperbolic sine of x.

coshf - ANSI C math - #include <math.h> - all ports

float coshf (const float x);

Compute the hyperbolic cosine of x.

tanhf - ANSI C math - #include <math.h> - all ports

float tanhf (const float x);

Compute the hyperbolic tangent of x.

expf - ANSI C math - #include <math.h> - all ports

float expf (const float x);

Compute e to the x power.

logf - ANSI C math - #include <math.h> - all ports

float logf (const float x);

Compute log base e of x.

log10f - ANSI C math - #include <math.h> - all ports

float log10f (const float x);

Compute log base 10 of x.

powf - ANSI C math - #include <math.h> - all ports

float powf (const float x, const float y);

Compute x to y power.

sqrtf - ANSI C math - #include <math.h> - all ports

float sqrtf (const float x);

Compute the square root of x.

fabsf - ANSI C math - #include <math.h> - all ports

float fabsf (const float x);

Compute the absolute value of x.

frexpf - ANSI C math - #include <math.h> - all ports

float frexpf (const float x, int *pw2);

Split x in to mantissa and exponent parts.

ldexpf - ANSI C math - #include <math.h> - all ports

float ldexpf (const float x, const int pw2);

Combine mantissa and exponent parts of a float.

ceilf - ANSI C math - #include <math.h> - all ports

float ceilf (float x);

Find the smallest integer not less than x.

floorf - ANSI C math - #include <math.h> - all ports

float floorf (float x);

Find the largest integer not more than x.

modff - ANSI C math - #include <math.h> - all ports

float modff (float x, float * y);

Split x in to integer and fractional parts.

setjmp - long jump - #include <setjmp.h> - ??? ports

int setjmp (unsigned char * jmpb);

Save the return address and sufficient task state

to allow implementation of co-routines or error

handlers that unwind the stack using longjmp.

Returns 0, which is reserved and cannot be used

by longjmp.

longjmp - long jump - #include <setjmp.h> - ??? ports

int longjmp (unsigned char * jmpb, int retval);

Return to the the location and task state previously

save in the jump buffer.  Any integer number except 0

may be passed as retval.

stdio.h

/*-------------------------------------------------------------------------

printf_small - standard character I/O - #include <stdio.h> - all ports

void printf_small (char *,...);

printf - standard character I/O - #include <stdio.h> - all ports

int printf (const char *,...);

vprintf - standard character I/O - #include <stdio.h> - all ports

int vprintf (const char *, va_list);

sprintf - standard character I/O - #include <stdio.h> - all ports

int sprintf (const char *, const char *, ...);

vsprintf - standard character I/O - #include <stdio.h> - all ports

int vsprintf (const char *, const char *, va_list);

puts - standard character I/O - #include <stdio.h> - all ports

int puts(const char *);

gets - standard character I/O - #include <stdio.h> - all ports

char *gets(char *);

getchar - standard character I/O - #include <stdio.h> - all ports

char getchar(void);

putchar - standard character I/O - #include <stdio.h> - all ports

void putchar(char);

string.h

/*-------------------------------------------------------------------------

strcpy - string manipulation - #include <string.h> - all ports

char *strcpy (char * d, char * s);

Copy the nul terminated source string s to the destination d.

strncpy - string manipulation - #include <string.h> - all ports

char *strncpy(char * d, char * s, int n);

Copy the nul terminated source string s to the destination d but

do not copy more than n characters even if this causes d to not

be nul terminated.

strcat - string manipulation - #include <string.h> - all ports

char *strcat (char * front, char * back);

Copy the nul terminated string back to the end of the nul terminated

string front, overwriting the nul and creating a concatenation of

the two with a single trailing nul terminator.

strncat - string manipulation - #include <string.h> - all ports

char *strncat(char * front, char * back, int n);

Copy the nul terminated string back to the end of the nul terminated

string front, overwriting the nul and creating a concatenation of

the two, but do not copy more than n characters, even if this causes

the result to no be nul terminated.

strcmp - string manipulation - #include <string.h> - all ports

int   strcmp (char * asrc, char * adst);

Compare two nul terminated strings asrc and adst.  Return a value < 0 if asrc

is less than adst.  Return a value > 0 if asrc is greater than adst.  Otherwise

return 0.

strncmp - string manipulation - #include <string.h> - all ports

int   strncmp(char * asrc, char * adst, int n);

Compare two nul terminated strings asrc and adst but do not check more than n

characters.  Return a value < 0 if asrc is less than adst.  Return a value > 0

if asrc is greater than adst. Otherwise return 0.

strchr - string manipulation - #include <string.h> - all ports

char *strchr (char * string, char ch);

Return a pointer to the first occurance of the character ch is string

or a NULL pointer if not found.

strrchr - string manipulation - #include <string.h> - all ports

char *strrchr(char * string, char ch);

Return a pointer to the last occurance of the character ch is string

or a NULL pointer if not found.

strspn - string manipulation - #include <string.h> - all ports

int   strspn (char *, char *);

strcspn - string manipulation - #include <string.h> - all ports

int   strcspn(char *, char *);

strpbrk - string manipulation - #include <string.h> - all ports

char *strpbrk(char *, char *);

strstr - string manipulation - #include <string.h> - all ports

char *strstr (char *, char *);

strlen - string manipulation - #include <string.h> - all ports

int   strlen (char *  );

strtok - string manipulation - #include <string.h> - all ports

char *strtok (char *, char *);

memcpy - string manipulation - #include <string.h> - all ports

void *memcpy (void *, void *, int );

memcmp - string manipulation - #include <string.h> - all ports

int   memcmp (void *, void *, int );

memset - string manipulation - #include <string.h> - all ports

void *memset (void *, unsigned char  , int );

time.h

/*-------------------------------------------------------------------------

mktime - time and date - #include <time.h> - all ports

time_t mktime(struct tm *timeptr);

asctime - time and date - #include <time.h> - all ports

char *asctime(struct tm *timeptr);

ctime - time and date - #include <time.h> - all ports

char *ctime(time_t *timep);

This table lists the ASCII characters and their decimal, octal and hexadecimal numbers. Characters that appear as names in parentheses [e.g., (nl)] are non-printing characters.

| ASCII Name | Description | C Escape Sequence |  | ASCII Name | Description | C Escape Sequence |
| --- | --- | --- | --- | --- | --- | --- |
| nul | null byte | \0 |  | nl | newline | \n |
| bel | bell character | \a |  | cr | carriage return | \r |
| bs | backspace | \b |  | vt | vertical tab |  |
| ht | horizontal tab | \t |  | esc | escape |  |
| np (next page) | formfeed | \f |  | sp | space |  |

Char  Dec  Oct  Hex | Char  Dec  Oct  Hex | Char  Dec  Oct  Hex | Char Dec  Oct   Hex

-------------------------------------------------------------------------------------

(nul)   0 0000 0x00 | (sp)   32 0040 0x20 | @      64 0100 0x40 | `      96 0140 0x60

(soh)   1 0001 0x01 | !      33 0041 0x21 | A      65 0101 0x41 | a      97 0141 0x61

(stx)   2 0002 0x02 | "      34 0042 0x22 | B      66 0102 0x42 | b      98 0142 0x62

(etx)   3 0003 0x03 | #      35 0043 0x23 | C      67 0103 0x43 | c      99 0143 0x63

(eot)   4 0004 0x04 | $      36 0044 0x24 | D      68 0104 0x44 | d     100 0144 0x64

(enq)   5 0005 0x05 | %      37 0045 0x25 | E      69 0105 0x45 | e     101 0145 0x65

(ack)   6 0006 0x06 | &      38 0046 0x26 | F      70 0106 0x46 | f     102 0146 0x66

(bel)   7 0007 0x07 | '      39 0047 0x27 | G      71 0107 0x47 | g     103 0147 0x67

(bs)    8 0010 0x08 | (      40 0050 0x28 | H      72 0110 0x48 | h     104 0150 0x68

(ht)    9 0011 0x09 | )      41 0051 0x29 | I      73 0111 0x49 | i     105 0151 0x69

(nl)   10 0012 0x0a | *      42 0052 0x2a | J      74 0112 0x4a | j     106 0152 0x6a

(vt)   11 0013 0x0b | +      43 0053 0x2b | K      75 0113 0x4b | k     107 0153 0x6b

(np)   12 0014 0x0c | ,      44 0054 0x2c | L      76 0114 0x4c | l     108 0154 0x6c

(cr)   13 0015 0x0d | -      45 0055 0x2d | M      77 0115 0x4d | m     109 0155 0x6d

(so)   14 0016 0x0e | .      46 0056 0x2e | N      78 0116 0x4e | n     110 0156 0x6e

(si)   15 0017 0x0f | /      47 0057 0x2f | O      79 0117 0x4f | o     111 0157 0x6f

(dle)  16 0020 0x10 | 0      48 0060 0x30 | P      80 0120 0x50 | p     112 0160 0x70

(dc1)  17 0021 0x11 | 1      49 0061 0x31 | Q      81 0121 0x51 | q     113 0161 0x71

(dc2)  18 0022 0x12 | 2      50 0062 0x32 | R      82 0122 0x52 | r     114 0162 0x72

(dc3)  19 0023 0x13 | 3      51 0063 0x33 | S      83 0123 0x53 | s     115 0163 0x73

(dc4)  20 0024 0x14 | 4      52 0064 0x34 | T      84 0124 0x54 | t     116 0164 0x74

(nak)  21 0025 0x15 | 5      53 0065 0x35 | U      85 0125 0x55 | u     117 0165 0x75

(syn)  22 0026 0x16 | 6      54 0066 0x36 | V      86 0126 0x56 | v     118 0166 0x76

(etb)  23 0027 0x17 | 7      55 0067 0x37 | W      87 0127 0x57 | w     119 0167 0x77

(can)  24 0030 0x18 | 8      56 0070 0x38 | X      88 0130 0x58 | x     120 0170 0x78

(em)   25 0031 0x19 | 9      57 0071 0x39 | Y      89 0131 0x59 | y     121 0171 0x79

(sub)  26 0032 0x1a | :      58 0072 0x3a | Z      90 0132 0x5a | z     122 0172 0x7a

(esc)  27 0033 0x1b | ;      59 0073 0x3b | [      91 0133 0x5b | {     123 0173 0x7b

(fs)   28 0034 0x1c | <      60 0074 0x3c | \      92 0134 0x5c | |     124 0174 0x7c

(gs)   29 0035 0x1d | =      61 0075 0x3d | ]      93 0135 0x5d | }     125 0175 0x7d

(rs)   30 0036 0x1e | >      62 0076 0x3e | ^      94 0136 0x5e | ~     126 0176 0x7e

(us)   31 0037 0x1f | ?      63 0077 0x3f | _      95 0137 0x5f | (del) 127 0177 0x7f