PG1                   SAFETY NOTICE

WARNING! POWER LINES CAN KILL YOU

DO NOT ERECT THIS ANTENNA NEAR ANY OVERHEAD WIRES, UNDER ANY CIRCUMSTANCES.  READ AND FOLLOW THESE INSTRUCTIONS CAREFULLY

- Do not erect this antenna near any overhead wires.  Assume all such wires to be

power lines and deadly.

- Do not transport this antenna from an assembly location to the installation site if you must travel near or under overhead wires.

- Request advice from your local power company if power wires are anywhere near the proposed location.

- If the antenna falls, DO NOT try and stop it.  Get out of the way.

- If any part of the antenna should touch overhead wiring, DO NOT TOUCH IT OR ATTEMPT TO MOVE IT.  Call the power company immediately for help.

- In the event of an accident involving power wiring DO NOT TOUCH THE VICTIM DIRECTLY.  Send someone for help.

- Select a site which limits public access to the antenna. During operation the antenna

has a high RF potential.  If any possibility exists that people or pets could touch the

antenna, place  a wooden fence around it.

- Choose a calm, dry day to erect the antenna.

- Always enlist the aid of at least one competent person in erecting the antenna.

- Do not use a ladder in the process of erecting your GAP Antenna.  A ladder is not needed and could be dangerous.

- Do not connect the coax until the antenna is firmly mounted.

PG 3

READ THE SAFETY NOTICE ON PAGE 1 BEFORE CONTINUING

CHAPTER 1: SITE CONSIDERATIONS

1.0 General

Ideally, it is best to locate the TITAN in a clear area, away from wires, metal buildings, fences and trees.

As a practical matter, many amateurs must compromise in locating their antennas.  This section contains specific guidelines to assist in making those compromises.

1.1 Site Safety

A) Reread  the safety notice now.  Stay away from power lines, they are life threatening.

B) Choose a site that it is not easily accessible to people or pets.

CONTACT WITH THE ANTENNA IS DANGEROUS AND CAN BE FATAL.

The counterpoise rods and the rest of the TITAN may be at high RF potential during operation.  If it is not possible to site the TITAN to prevent access, then it should be placed high enough such that people

cannot reach it or it should be surrounded by a fence.

1.2 Nearby Wires and Antennas

- In general, any vertical antenna can exhibit mutual coupling with any other vertical metal structure or

wire if placed within a few wavelengths or the structure approaches resonance at the operating

frequency.

- Try to avoid metal objects which may be within 30' of the proposed GAP installation site.  These may include wires, towers, down spouts, screened porches, feedline from other amateur antennas or TV

antennas, metal pipes on your property or adjoining properties.  Naturally, if these metal objects are

short you can get closer than 30'.

- Nearby horizontal wires or structures may affect the performance of a vertical antenna, but they are

not as likely to, as a vertical structure is.

1.3 Buildings

- It is best to locate the antenna as far from the home as possible, to minimize interaction with house

wiring, and RFI to consumer electronics.

- Metal walled or roofed buildings can affect antenna operation.  If you have no choice, your GAP

should be located at a corner of the building, rather than broadside.  In any case, the TITAN should

be tested first away from the building.  See Section 6.0.

- Stucco buildings may have metal mesh in their walls and should be viewed as a metal structures,

until proven otherwise.

- Mobile homes or RV's are a special case, which involve individual experimentation.  Test the

antenna  on  the ground before attempting installation near or on the RV.  Mounting above the

roof line is preferred.

1.4 Guying

The TITAN is designed to withstand substantial winds unguyed.  Guys are a form of insurance, however,

which we recommend.  Four nonconductive guy ropes should be fastened above the center insulator.

Use a stainless clamp or optional guy clamp available from GAP.  Leave some slack to allow for

temperature changes.  Guys should be used for roof mounting.  Do not rely on a chimney mount or

tripod to support the TITAN, even moderate winds can produce enough force to damage the mount or

the chimney.

PG5

CHAPTER 3: ASSEMBLY

3.0 General

The assembly of the GAP TITAN requires no special tools and a nut driver has been supplied

for your convenience.  Plastic stand-offs that support the tuner rods are attached to the

aluminum mast at their approximate proper positions to simplify assembly.  Do not remove these

at this time.  Before starting assembly, check the various parts in the shipping container against

the pictorial parts list in figure 2 to establish all parts are present.  Next review Figure 1 which depicts an assembled TITAN.  As you proceed to assemble your Titan, use this diagram.

NOTE: That in the assembly instructions, when a single hole is identified on a tuner rod it is

thru drilled.  Thru drilled holes provide you with a backup should you accidentally strip a hole

by over tightening.

We found that telling you to insert a screw and washer gets repetitive, therefore whenever a

screw is called for include a washer as well.  When attaching jumpers and transitions, the

washer should be placed between the ring terminal and the tube.  Not between the screw head

and ring terminal.

When we refer to the "GAP" we are referencing the center insulator with the yellow band.

3.1 Space Required

To get started with the assembly, you will need a flat space approximately 30' in length.

A driveway or patio surface is ideal.  The key to an easy assembly is room to move, a surface

which allows you to find the screws you drop and careful attention to the directions.  Extra

crews have been provided because we know how lawns like to eat screws.

3.2 Mast Assembly

Standoffs are positioned on the various mast sections at their approximate final positions.

Do not loosen the clamps.

A) Locate the Main Section.  Place the Main Section on a flat surface.  Stretch out the coax that protrudes from each end.  NOTE The coax that goes to the top of the antenna has a yellow ring terminal.

B) Locate the Top Section.  Place the end without the notch over the coax cable with the yellow terminal.

- Slide the Top Section into the Main Section.  Gently push the Top Section into the Main

Section beyond the matching holes, until the yellow terminal and spade connectors are exposed.

- Plug the CAP unit onto the spade connectors found on the coaxial cable.  Make sure the

male spades on the CAP unit align with the female spade terminals on the coax.

- Pull the Top Section back out and align it's four screw holes with the four holes in the Main

Mast Section.  Insert 4 screws.  Snug all screws first before tightening one particular screw.

NOTE This procedure should be repeated wherever multiple screws are inserted.  Snug

first then tighten

- Place the yellow ring terminal at the top of the antenna through the slot and over the nearby

drill hole.  Insert a screw and tighten securely.  WARNING: Make sure the CAP unit is pushed

down below the screw, so it does not crack the CAP unit when you insert it.

G) Locate the black dust cover and place it over the Top Section.

PG7

A)Locate the two short standoffs on the Main Section. Slide the 51" Top tuner rod thru these standoffs so the screw holes are towards the GAP.  Loosen and adjust the standoffs so the

tuner rod is parallel to the mast, now tighten the clamps.

B) Locate the drill hole 10" from the end of this tuner rod.  Position this hole between the two standoffs and insert a screw and tighten.  This is a stop screw

- Slide the tuner rod toward the GAP.  Locate a black jumper.  Remove the screw holding

the lower GAP lead, see fig. 3.  Place the black jumper under the screw with the GAP lead,

reinsert and tighten.

- Attach the other end of the jumper to the hole at the end of the Top tuner rod with a

screw and tighten.

- Locate the four standoffs on the Mid section just below the GAP.  Loosen their clamp.

Form these four into a cross, perpendicular and immediately below the GAP.  Tighten the

clamp securely.

F) Locate the four standoff assembly at the top of the Lower Section.  Form these four

into a cross perpendicular to the mast.  Tighten the clamp lightly.  Now locate the longest

standoff  on the upper cross assembly.  Rotate the lower cross assembly until it's longest

standoff is in line with the one on the upper unit.  Tighten the clamp.

G) Take the four 102" Mid tuner rods and insert a screw in the hole 10" from the end of

each rod and tighten.  This a stop screw.

H) Slide a 102" rod thru each standoff in the top cross, starting with the end opposite the

screw just inserted and then into the bottom standoffs.  Each rod should be parallel to the

Main mast.  You may have to adjust the lower cross unit to achieve parallel rods.  Each rod

should stop at the stop screw.

I) There are four yellow transition wires at the GAP, one longer than the other three.  Attach

one to each Mid tuner rod with a screw and tighten.  The longest wire attaches to the tuner

rod on the longer standoff.  All wires should not be taut.  If you find a wire is taut it may be

necessary to rotate the two cross units to relieve any tension on the transition wires.

J) Locate the extension rod with the attached slotted extender.  Locate the Mid tuner on

the longer standoffs.  Slide the slotted extender over the bottom end of this 102" rod until it

butts against the extension.  Rotate the extender until the hole in the Mid tuner rod lines

up with the slot in the extender.  Insert a screw into this hole and slot and tighten.

See figure 4.

K) Locate the remaining extender and place it over the Mid tuner rod opposite the tuner rod

just installed.  Align the slot in the extender with the hole on the tuner rod and secure as in J.

It should extend about 4.5 inches and has no additional rod inserted into it.

L) Loosen the clamp on the short pair of standoffs on the Lower section.  Rotate this pair until

they line up with the Mid tuner rods without the extenders.

M) Take the last two short standoffs on the Lower section, loosen each clamp and orient

one of these standoffs so it is in line with one from the pair above it.  Orient the other so it

is in line with the remaining standoff of the pair.  Tighten the clamps.

PG 9

5.2 COUNTERPOISE ASSEMBLY see figure 6

A) Attach the stainless clamp to the assembled Counterpoise bracket.  Place the bracket

against the Lower Section in between the two sets of screws at the base.

- Tighten the clamp securely

- It is recommended that the Counterpoise Hoop assembly, be deferred until the TITAN

has been installed in it's final position.  RAISING the antenna with the hoop installed is

cumbersome and can damage the antenna.  The following section is easier to complete

after the antenna has been mounted. Check section 6.0 before continuing.

5.3 COUNTERPOISE HOOP

- Locate the 80" counterpoise rods.  There are drill holes on both ends.  Slide each rod

into the Counterpoise bracket see figure 5 & 6. Make sure the rod with the yellow end cap

slides into one side of the aluminum tube, not the PVC.

- Align the hole in the 80" rods with the hole in the counterpoise tubes.  Insert a screw in

both holes and tighten.  This step is optional if you plan on frequently raising and lowering

your antenna.

- Locate the 3 Counterpoise End Caps and the 35 foot copper Counterpoise Hoop with

1 ring terminal.  The End Caps have a rivet in them.

- Each End Cap also has a thru drilled hole close to one end.  Thread the end of the

copper wire without the ring terminal thru these holes in the End Caps.

PG 11

IMPORTANT  The length of the Counterpoise Hoop controls the center frequency on 40m.

The longer the Counterpoise wire is, the shorter the Dacron rope is and the lower the

resonant frequency will be.  Likewise the shorter the length of the Counterpoise Hoop the

higher the resonant frequency will be and the longer the Dacron rope will be.  Adjust the Counterpoise Hoop and check the frequency with your VSWR meter on 40m.  Adjust the

length to suit your preference on 40m.  Keep in mind that as you adjust the overall length

of the Counterpoise hoop wire the loop created between the split bolt and the ring terminal

on the Dacron should remain about 2”

5.4 POLE MOUNT ASSEMBLY-REFER TO FIGURE 7

A) Locate the 3"x12" aluminum plate, the six U-bolts and twelve nuts.

B) Insert the U-bolts into the plate as shown in figure 7

C) Locate the six collar insulators.  Place each under a U- bolt.

D) Finger tighten the nuts on the ends of all the U-bolts.

E) Using a 7/16" wrench tighten the U-bolts until the collars are just held in place.

- Take the assembled unit and slide it over the base of the antenna.  They should slide

freely.  If not, they are overtightened and the U-bolts should be loosened.

G) Continue to slide this unit up the base, until the collar on the first unit butts against the

lower portion of the antenna.  Tighten the nuts securely on the top unit.

H) Make sure the nuts that hold the Lower section to the mount plate assembly are tight.

I) Locate your 11/4" mast.  Carefully slide your mast thru the 3 vacant insulating collars until

your mast pipe is flush with the top of the mount plate assembly.  Tighten all U-bolts with

a 7/16" wrench.

5.5 COAX TAIL

A) Bring the coax tail out through the exit hole in the side of the Lower Section. YES, it is

important for the coax to exit through the hole in the side.  Do not bring it straight out

the bottom.  Locate the PL259 connector with adapter.  Attach the connector to the

coax.  See the ARRL Handbook if you are unsure of the procedure.  In your final

installation, make sure the connector does not touch your support mast.

B) If properly connected, an ohm meter will read "open" when placed from centerpin

to shell.

NOTE If your pipe is slightly oversized the PVC collars have been slit to allow for

expansion.  Operating without these insulators can affect performance.

PG13

6.1 GENERAL

A ham band transceiver and SWR meter are required for these tests.  It is recommended that

you use the minimum necessary power for the measurement.  If possible, use an SWR bridge separate from that provided in your transceiver.  Using a pencil, record your data in the space provided below.

6.2 FIRST OPERATION

A) If the TITAN has been assembled properly it will resonate close to the selected frequency on 75/80 meters.  You should see a useable bandwidth in excess of 100 KHz under normal

operation.  Using minimal power, 10 watts or less;

Record the minimum VSWR on 75/80.            ___________________

2:1 VSWR Hi frequency         ___________________

2:1 VSWR Low frequency      ___________________

B) Using minimal power, determine the resonate frequency on 40 meters.

Minimum VSWR         ____________________

2:1 Hi  frequency           ____________________

2:1 Low frequency        ____________________

C)30 meters is next.   Freq.     10.100          ___________________

10.125          ___________________

10.150          ___________________

D)20 meters                             14.00            ___________________

14.175          ___________________

14.350          ___________________

E) 17 meters                            18.068           ____________________

18.118           ____________________

18.168           ____________________

F) 15 meters                            21.00             ____________________

21.225           ____________________

21.450           ____________________

G) 12 meters                           24.890           ____________________

24.990           ____________________

H) 10 meters                            28.00            ____________________

28.50             ____________________

29.00             ____________________

CHAPTER 7 TIPS AND TROUBLE SHOOTING                                           PG 14

7.0 GENERAL

The TITAN DX has been designed to operate on the 8 bands specified.  Operation outside the specified bands may damage the antenna.

Use of an antenna tuner is not required nor recommended.  Tuners will not improve the performance of the antenna, although they may permit a solid state transmitter to put out more power.

Operation of the antenna using a tuner on any frequency where the VSWR exceeds 2:1 may damage the antenna.  Use when VSWR is less than 2:1 is acceptable.

7.1 MALFUNCTION

A) If the antenna fails to resonate on the 75/80 meter band the CAP unit plugged on at the top of the antenna may not be making proper contact or was inadvertently shorted when the screw was inserted.

B) If all your standing waves are high, double check the PL259 connector at the base of the antenna and make sure it is open from center pin to shield.

C) If only a couple of bands are high eliminate the following possibilities;

- Bad coaxial feedline.  If the coax has been in use for some time, it may be

contaminated.  Place a 50 ohm dummy load at the far end of your feedline, in

place of the antenna.  Any indication of varying VSWR or a standing wave

greater than 1:1 suggests defective coax.

- Mutual coupling with nearby vertical metal objects may detune the TITAN.

Check to see if any of the items suggested in section 1.2 & 1.3 apply.

3)  Transceivers with built in SWR bridges may not correctly indicate when their

power reduction circuits take over.  Retest with a separate VSWR meter.

- The transceiver or transmitter may be emitting a spurious signal in addition to

the desired signal.  Retest using the lowest possible power level.  If possible

try another rig.

If you are unable to solve the problem, contact the factory for assistance.  Please have section 6.2 filled in and handy when you call.  We do not charge for assistance and our phone number is (561) 571-9922.

PG12

FIGURE 7

6.0 PRETEST PROCEDURE

It is always best to test the TITAN at ground level before elevating it.  Pretesting is not difficult

and may save time and effort in the total process.  This is particularly true if the antenna is to be significantly elevated.

A) Locate an open space.

B) Obtain an 11/4" pipe 5' long.

C) Attach this pipe to the TITAN see section 5.4.

D) Obtain 3 lengths of rope 25-30' long.

Attach ropes just above the GAP center insulator.

F) Dig a small hole or insert a small diameter tube or large screwdriver in the ground,

G) With help raise the antenna until it is vertical.

H) Place your 5' pipe in the hole or over the screwdriver or tube, this will keep the base in place.

I) Secure the temporary guy ropes.

J) Complete the hoop assembly see section 5.3.  For this test it is not necessary to put screws into the Counterpoise rods.

PG 10

E) Locate the wire extension with the two ring terminals

F) Take the ring terminal from the Counterpoise Hoop wire and one terminal from the wire extension.  Place both terminals over the drill hole at the end of the 80" counterpoise rod that has the yellow end cap and is attached to the aluminum tube on the Counterpoise bracket.  see figure 6.  Insert a screw attaching these terminals to the Counterpoise rod.

G) Circle the ends of the Counterpoise rods with the Counterpoise Hoop placing an End Cap on each Counterpoise rod as you circle.

H) Find the Dacron cord with the ring terminal.  Feed the end of the Counterpoise wire thru the split bolt, the ring terminal on the Dacron cord and back through the split bolt.  The distance between the split bolt and the ring terminal on the Dacron should be about 2” or running the wire through the split bolt,  the ring terminal on the Dacron and back through the split bolt creates, roughly a 2” loop.

I) Thread the Dacron cord thru the vacant ring terminal of the wire extension.  Pull the cord until the Counterpoise Hoop has no slack in it but, do not over tension the hoop.  For starters your Dacron should be about 12”.  If necessary slide some of the hoop wire through the split to either create more length or take up slack.  Tie a temporary knot in the Dacron cord to the ring terminal on the wire extension.

PG 8

N) Slide the shortest Lower tuner rod through the closest spaced standoffs, with

the drill hole closest to the GAP.  Locate a black jumper and attach one end to the top

of the short tuner rod with a screw and tighten.

O) Slide the longer lower tuner rod thru the remaining short standoffs, again, so

the screw hole is closest to the GAP.  Take the remaining black jumper and attach

it to the top of this rod with a screw and tighten.

P) Take the other ends of each black jumper and attach it to the Mid Tuner rod directly above with a screw and tighten.  These jumpers should be loose.  If they

are taut you can raise or lower the position of the clamp on the short standoff pair

to remove any tension.  Proper positioning can be achieved by making sure the bottom

of these two Mid tuner rods are in the same plane as the tops of your

Lower tuner rods.

CHAPTER 5: COUNTERPOISE AND HOOP ASSEMBLY

5.0 GENERAL

The Counterpoise and hoop assembly includes a Counterpoise support bracket,

4-80" rods, Counterpoise Hoop - a 35' length of copper wire with a ring terminal,

a 4' length of Dacron with a ring terminal, 3 counterpoise End Caps and a 4' 9"

fixed wire extension with 2 ring terminals.

5.1 Counterpoise Bracket Assembly see figure 5.

A) Locate the Counterpoise bracket.  It is partially assembled.  Locate the

3/4" x 9" long PVC section with the 2 rivets inserted.

B) Push a 11/4" screw thru one of the vacant holes in the aluminum bracket.

Place one of the drill holes in the PVC tube over this screw.

C) Push a second screw thru the remaining vacant hole in the aluminum bracket

and then through the remaining vacant drill hole in the PVC tube.

- Attach lock nuts to each screw and tighten both securely

PG 6

H) Locate the Mid Section.  It has 4 standoffs attached to one end.  Slide the end with

the 4 standoffs over the coax tail protruding from the Main Section center insulator.

I)  Align the holes on the insulator with the holes in the Mid Section.  Place a screw and washer through the remaining ring terminal on the short yellow GAP lead coming out

from the center insulator.  Insert this screw in the hole closest to where the lead comes

out of the center insulator.  See figure 3.  Insert the remaining 3 screws and tighten.

Leave the standoffs as is, for the moment.

J) Locate the Lower Section.  It is a double wall and triple walled section for added

strength.  It has four long standoffs at one end.

K) Slide the end with the standoffs over the coax tail and partially over the Mid Section.  Align the 4 holes, insert 4 screws and tighten securely, remember to snug them all first.

Do not attach the PL259  connector.

CHAPTER 4: TUNER ROD ASSEMBLY

4.0 GENERAL

There are four 102" Mid tuner rods,  two Lower tuner rods 30" and 60" and one 51"

Top tuner rod.  Two extensions complete the tuner rod package.  The standoffs have

been prepositioned at the factory for your convenience.  When orienting these

standoffs you should not have to move them along the mast, but simply loosen the

clamp and lever them out, so they are perpendicular to the mast.  If you should slightly

shift their relative position along the mast don't despair.  Slight movement is not critical.

PG 4

CHAPTER 2: ANTENNA MOUNTING

2.0 General

The TITAN will accommodate a variety of mounting situations, some of which

are described below.  The preferred mount is a pole mount.  It is simple and

avoids the hazards of a roof top installation.  Electing to roof mount the antenna

is solely your decision and extreme caution should be exercised.

If you elect to elevate the antenna, always pre-test the antenna on the ground

first.  See Section 6.0  Locating a loose connection when the antenna is on top

of a 40' mast is not easy!!

2.1 Pole Mounting

The TITAN is designed to be pole mounted.  A mount plate assembly has

been provided to attach the TITAN to a pole of your choice.  It is recommended that you select a very heavy gauge steel pipe.  The outside diameter of which should

be 1.25".  This pole may be attached to the side of a structure ie house

or garage for additional support.  If you elect to side mount, be certain your pole

extends above the roof line to allow clearance for the Counterpoise hoop.  Three foot clearance is typical.

If you elect to mount the TITAN on a pole in the yard, the pole should be mounted

in an 18" diameter hole 3 feet deep or more and filled with concrete.  It is far

easier to erect the antenna with your support pole attached, rather than trying to

lift the TITAN onto your support pipe.  Thus your support pole should be such that

it is removable from the concrete.  To achieve this, procure a 3' length of 1.25" schedule

40 PVC.  Make sure it will sleeve over your support pipe, if it is not large enough slit the pipe lengthwise and slide it over your pipe.  Cover the slit with

tape and place the PVC covered pipe in the 3' hole and fill with concrete.  When

the concrete has set remove your support pipe.  You can now drop your support pipe

into the hole you created by your PVC form.

2.2 TOWER MOUNTING

The TITAN may be mounted to a tower.  Do not clamp directly to the tower.  Use

the Mount Plate Assembly to insulate the TITAN from the tower itself or the

support.  The TITAN must be placed at the top of the tower and not parallel with

it.  You may experience reduced bandwidth on a band if you tower mount the

TITAN.  This is generally a result of the tower exhibiting a resonance for that frequency.

2.3 TRIPOD/CHIMNEY MOUNT

The TITAN may be mounted in a tripod or to a chimney mount.  Use the mount plate assembly to insulate the TITAN from the tripod or chimney mount.

CAUTION The TITAN and mount are in excess of 29’ tall.  Under no circumstances

should a tripod or chimney mount exist without guy ropes.  Guy the Antenna!

PG 2

TITAN DX ANTENNA

Congratulations on your purchase of the GAP Titan antenna. You soon will enjoy the ultimate in vertical antenna technology.  Your GAP antenna has been designed and manufactured to provide superior performance, and a long trouble free life.

GAP technology produces highly efficient, wide bandwidth performance. As  a result, no tuning is required in most amateur installations.  This manual is organized to minimize the amount of time necessary to assemble and install your GAP vertical.  It is recommended that you follow the instructions and use the figures as a guide.

Before beginning assembly, take a few minutes to read though the site selection chapter and to review the SAFETY notices. Please refer to Figure 1, the Titan antenna, as you proceed with the assembly. Locate the parts, from the parts list in Figure 2.  Call GAP direct if you find anything is missing.

The TITAN DX has been designed to operate efficiently on eight bands at 1500 watts PEP or less.  The TITAN cannot be run continuously ie. Amtor, RTTY etc...at maximum power on 75/80m.

The use of an antenna tuner is not required.  Tuners will not improve the performance of the TITAN, however they may permit a solid state transmitter to put out increased power.  Operation of an antenna tuner when the VSWR is 2:1 or less is permitted.  High power operation outside the specified bands using a tuner can damage the antenna.

CHAPTER 1:  SITE CONSIDERATIONS

SAFETY, nearby structures, buildings, guying

CHAPTER 2:  ANTENNA MOUNTING

Pole, tower, or chimney

CHAPTER 3:  MAST ASSEMBLY

Space required, Mast Assembly, Step by Step

CHAPTER 4:  TUNER ROD ASSEMBLY

Top, Mid, Lower and Extensions

CHAPTER 5    COUNTERPOISE AND MOUNT ASSEMBLY

CHAPTER 6:   INITIAL TEST

First Operation...a place to record VSWR data

CHAPTER 7:   TIPS AND TROUBLESHOOTING

READ THE SAFETY NOTICE ON PAGE 1 BEFORE CONTINUING