ECSE 6961: Fundamentals of Wireless Broadband Networks

Homework Problem Set: 3

(Lecture Slide Set: Wireless Channel)

Due Date: March 4th 2007; [40 points]

- [dB, dBm, dBi]: [5 pts] A transmitter produces 50 W. Express in units of (a) dBm and (b) dBW. If this is applied to a 12 dBi gain transmit antenna at 900 MHz, find the received power Pr in dBm at a distance of 100m. What is Pr (10 km) in dBm? Assume unity gain receive antenna. Hint: Recall the path loss formula:

- [Path Loss Effects, Small Cells, Cell Edge]: [10 pts] Consider a user in the downlink of a cellular system, where the desired base station is at a distance of 900 meters, and there are numerous nearby interfering base stations transmitting at the same power level. If there are 3 interfering base stations at a distance of 1 km, 3 interfering base stations at a distance of 2 km, and 10 interfering base stations at a distance of 4 km, use the empirical path loss formula to find the signal-to-interference ratio (SIR, i.e. the noise is neglected) when ( = 3, and then when (= 5. Explain the implications of your results.

Empirical Path Loss Formula:

the path loss exponent  ( and the measured path loss Po at a reference distance of do. You don’t need the values of Po and do to solve the problem.

- [Shadowing, Outage, Modulation Choice:] [15 pts] Consider a WiMAX base station (BS) communicating to a subscriber, with the channel parameters: path loss (() = 3.5, Po = −35dB, d0 = 1m, shadowing parameter ((s) = 5dB. We assume a transmit power of Pt = 1 Watt (30 dBm), a bandwidth of B = 10 MHz. Due to rate 1/2 convolutional codes, a received SNR of 14.7 dB is required for 16QAM, while just 3 dB is required for BPSK. Finally, we consider only ambient noise with a typical power spectral density of No = −173dBm/Hz, with an additional receiver noise figure of Nf = 6 dB (noise from all other sources).

The question is this: At a distance of 400 meters from the base station, what is the likelihood that the BS can reliably send BPSK or 16 QAM? {Hints: Find receive power, receive noise, compare to thresholds for BPSK/16QAM. The effect of the shadowing will matter. Use the simple empirical shadowing model below}:

- [Doppler spread] [5 pts] Consider mobile nodes moving at speeds (v) of 60 km/h (car on a state road), 200 km/h (high speed train), 400 km/h (airplane taking off/landing). Consider two carrier frequencies fc = 900 Mhz (2G band) and 2.5 GHz (a WiMax band). What is the Doppler spread for each combination of v and fc ? What is the channel coherence time (Tc) in each case?