ECSE 6961: Fundamentals of Wireless Broadband Networks

Homework Problem Set: 4

Due Date: April 1st 2007; [50 points]

- [Constellations & Orthonormal bases]: [10 pts]

- [Signal Space]: [10 pts]

3. [Matched Filter] [10 pts] Find the matched filter for the following waveforms. (Optional: plot them by computer or roughly by hand to compare how it looks w.r.t. the original pulse)

4. [Modulation perf.]: [10 pts] We saw in class that:

Assume a target PE of 10-5. What is the excess required SNR = Es/No (in dB) as we move from BPSK to 64PSK? Explain.

(Hint: Recall that in BPSK, the constellation points are at +sqrt(Es) and –sqrt(Es). dmin will reduce. Note: MPSK is a circular constellation. You can also assume the exponential approximation for the Q function if necessary.)

5. [Pulse Shaping:] [10 pts] Consider the raised cosine filter (and formula) mentioned in the class slides. Explain the quantitatively the key tradeoffs (vs. the Nyquist Filter) for roll off factors of r = 0, 0.5 and 1.